## Slide 1
Hydra 4 architecture overview
Dave Gillespie, daveg@synaptics.com
Last updated: October 29, 2026 (Originally written in January 2022)

## Slide 2: WORK IN PROGRESS!
This is a preview of an internal document that we use within Synaptics to describe our Hydra vector arithmetic processor
We are preparing a more public-friendly version, without the references to past versions, specific chip projects, and other stuff that is only of interest within Synaptics
The cleaned-up document, and the Hydra User’s Guide itself, as well as the analogous materials for our Chimera processor, will shortly be available here:
  github.com/synaptics-hydra
  github.com/synaptics-chimera
Until then, you are welcome to preview here the “raw” version …
Thank you!
— Dave Gillespie, daveg@synaptics.com

## Slide 3: Hydra 4
Architecture overview
  Introduction
    What, why, where
  Using Hydra
    Examples, registers, instructions, types, modes, …
  Hardware and implementation
    Block diagrams, theory of operation, interesting details

## Slide 4: Hydra 4
Architecture overview
  Introduction
    What is it
    Why we need it
    Where it came from
  Using Hydra
  Hardware and implementation

## Slide 5: Hydra 4 at a glance
The Hydra arithmetic coprocessor adds powerful vector arithmetic capability to a small embedded MCU (such as SiFive RISC-V E, ARM Cortex-M, or Synaptics Chimera)
  It adapts “big CPU” vector capabilities to the scale, power, cost, and size of embedded systems
Synaptics products use Hydra for many things, such as:
  Accelerating touch algorithms • Signal processing • Fingerprint image processing + matching
Hydra 4 significantly accelerates many operations including:
  Arithmetic on vectors, matrices, and images
  Matrix multiply • Linear algebra • FFTs
  1D and 2D convolutions and median filters
  Neural networks • Encryption and hashing
  Pseudo-random numbers • Trig functions
  Bit operations • Packing data into few bits
  And much more
Data RAM
(Interleaved banks)
System bus
Bank intf
Host intf
Registers
Decode
Control
Bank intf
Bank intf
Bank intf
mask channel
SPU channel
src1 channel
src2 channel
misc channel
dest channel
ALU
(fixed-point and floating-point datapath)
Stored program unit
Mem intf
Embedded CPU
Hydra 4

## Slide 6: Hydra
Hydra is an arithmetic accelerator for small Synaptics chips
It works alongside a chip’s CPU such as Chimera, RISC-V, ARM, or Xtensa
Hydra does bulk calculations on vectors/arrays/matrices/images of data
Hydra version 1, 2, or 3 is found in many “high-performance” Synaptics touch chips
  DIG2401 and DIG2403–DIG2408 (touch controllers)
  TD7800, TD7850, TD7875 (automotive TDDI)
  B1422 “Prometheus” and B1442 “Triton” (fingerprint with match-in-sensor)
Hydra 4, the latest version, appears in our newest chips
  First up: The SB7900 “SmartBridge” automotive chip and the DIG2409 “Byrd” and DIG2411 “Denmarke” touch controllers
“Hydra” of Greek mythology
Notes: This drawing of the Hydra came from ChatGPT Images.

## Slide 7: Hydra in context
Example: Hydra 4.0, as integrated into the DIG2409A “Byrd” chip
  The host CPU is an “E76” RISC-V core from SiFive
  The E76 connects to the chip’s data RAM as tightly-coupled (“DTIM”) memory
  Hydra connects to the CPU as a register-mapped peripheral via the AHB bus
  Hydra also connects directly to the same data RAM
  Optionally, Hydra can drive the data bus to access other parts of the chip (omitted on Byrd A0)
To touch analog

## Slide 8: Vector processing on a small budget
Hydra is a vector processor: It operates on whole arrays (“vectors”) of data at a time
One instruction for a vector processor is like a complete loop in a program
The single instruction “VADD A, B, C” might do all this:
for (i = 0; i < N; i++) { A[i] = B[i] + C[i]; }
A big vector processor (e.g., x86 SSE / AVX, ARM Neon, or RISC-V “V”) will have wide registers and multiple arithmetic units to do all these additions at once, in parallel
Down in our price range, a vector processor must work through the vector iteratively
But it can work much more efficiently than ordinary CPU firmware can do
B[0] | B[1] | B[2] | B[3] | B[4] | B[5] | B[6] | B[7] | ∙∙∙ | B[N-1]
+ | + | + | + | + | + | + | + |  | +
C[0] | C[1] | C[2] | C[3] | C[4] | C[5] | C[6] | C[7] | ∙∙∙ | C[N-1]
↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ |  | ↓
A[0] | A[1] | A[2] | A[3] | A[4] | A[5] | A[6] | A[7] | ∙∙∙ | A[N-1]
A[0]
A[1]
A[2]
A[3]
A[4]

## Slide 9: DIG2409 “Byrd”
Byrd has dramatically higher computation needs (“MIPS”) than previous touch chips
  Foldable phones  Touch images twice as large
  Gaming phones  Crazy high frame rates!
  AFE improvements  FFTs per-frame or per-burst
Byrd replaces our Chimera CPU with a powerful RISC-V CPU: SiFive’s E76
  An 8-stage pipeline that can clock at 400 MHz (in TSMC’s 40nm Embedded Flash process)
  Full dual-issue superscalar operation, optimized for computational performance
  It’s a beast — at least 3x bigger than either Chimera or Hydra, but we needed the MIPS!
Even the E76 was barely enough to meet Byrd’s anticipated MIPS needs …
  So, once again, we augment the main CPU with Hydra
  A perfect time to refresh and modernize Hydra  “Hydra 4.0”

## Slide 10: SB7900 “SmartBridge”
The SB7900 chip, for large automotive touchscreens, also has Hydra 4
  SB7900 shares a lot of Byrd’s architecture, again using E76 as its main CPU
Hydra 4 was included in SB7900 for more speculative reasons
  The auto industry cares much more about safety and robustness
  It is beginning to get very serious about cybersecurity, too
  Hydra 4’s AES, public-key, and SHA2 cryptographic functions should prove invaluable for these
In fact, the SB7900 chip taped out before Byrd
  Byrd is too expensive for any but the most demanding applications
  Byrd was shelved for a period, but it eventually taped out in 2024
  In any event, most modern Synaptics touch chips have shipped with Hydra, and our future ones will ship with Hydra 4

## Slide 11: Hydra 4
A modern vector coprocessor that is built for small chips like ours
A 32-bit-oriented architecture that fits well with ARM, RISC-V, and modern Chimera
A clean design that is easy to use
A fresh implementation that is easy to maintain
Ground rules:
  Stay true to Hydra’s and Chimera’s “nimble” roots: Small, austere, efficient, flexible, agile
  Hydra is not trying to be as fast as RISC-V’s big “V” extension or ARM’s Neon
    But it is significantly faster than doing the same operations in microcontroller firmware
    And Hydra 4 is a lot faster than Hydra 3
  Keep it small and cheap: Roughly comparable in size to Hydra 3
  It is okay to break compatibility with Hydra 1/2/3, but make it easy to port existing firmware
  Fulfill longstanding feature requests from Hydra’s past users
  Look toward new application areas such as ultra-low-power small neural networks

## Slide 12: First implementation: Hydra 4.0
Hydra 4.0 is a ground-up rewrite of Hydra’s Verilog RTL and test suite
  The latest version is now Hydra 4.2.1
The Hydra 4 User’s Guide defines quite a lot of functionality
  (Available soon on github.com/synaptics-hydra)
  We implemented most of this spec — as much as was possible — in time for SmartBridge tapeout
  Starting with the things needed for today’s algorithms and directly anticipated needs
  Beyond that, we will continue adding features and improvements as Hydra 4.x evolves
Hydra 4 aims to be “only fractionally larger” than Hydra 3
  Byrd and Keys synthesis results show Hydra 4.0 is 10–15% larger than fully configured Hydra 3.3
Hydra 4 is able to clock as fast as Byrd’s SiFive E76 host CPU (~400 MHz in 40nm EF)
  Hydra shouldn’t be what limits our clock speed
  Hence, Hydra 4 is much more extensively pipelined than Hydra 3

## Slide 13: Major improvements vs. Hydra 3.3
Much faster (higher max MHz, and also does much more per MHz)
  Hydra 4 is twice as fast (per MHz) for floating-point and 32-bit integer computations
  Multiple 32-bit-wide channels to RAM • (Potentially) less instruction start/stop overhead
Much easier to use: No hairy macros or “Hydra assembler” required
Easy to integrate in hardware, with a clean, maintainable, 32-bit implementation
Much more flexible programming model:
  Instructions can mix any combination of integer, fixed, float, and packed data types and any combination of addressing modes
  FFTs, median filters, and sorting are now affordable standard features
Many new capabilities:
  Complex numbers • Half-precision floats • Sparse vector masks
  Pseudorandom numbers • Packed ints & floats • Generalized convolutions
  Neural networks • Pattern generation • Generalized matrices
  Cryptographic algorithms • Simplified SPU • Multi-threaded usage

## Slide 14: Detailed improvements: General architecture
 | Hydra 3.3 | Hydra 4.2
Memory interface | Direct-style only | Choice of direct, AHB, or mix
Width of memory interfaces | 16 bits | 32 bits
Max memory data bandwidth | 64 bits/cycle | 128 bits/cycle
Memory address range | Up to 219 (512K) bytes | Up to 232 (4G) bytes
Host CPU interface | Chimera-style only | Chimera, AHB, APB, or direct
Width of host CPU interface | 16 bits | 32 bits
Width of arithmetic datapath | 16 bits | 32 bits
Hardware integration | Tricky timing and interfacing | Much easier
Compatibility | Mostly backward compatible through 10 years to Hydra 1.0 (in both the RTL and the user-visible architecture) | A fresh, clean new design inside and out (A “Hydra 3 compatibility” mode assists firmware porting)

## Slide 15: Detailed improvements: Cost and performance
 | Hydra 3.3 | Hydra 4.2
Size of Hydra core | Approx. same as Chimera 4; Approx. 1/2 of ARM Cortex-M4; Approx. 1/3 of SiFive E76 | Similar; fractionally larger
Maximum clock rate (40nm EF) | < 300 MHz? | At least 400 MHz
Speed of 16-bit integer math | 1 result per cycle | At least 1 result per cycle
Speed of 32-bit integer math | 1 result per 2 cycles | 1 result per cycle (2x faster)
Speed of floating-point math | 1 result per 2 cycles | 1 result per cycle (2x faster)
Time for a typical float vector operation of size N | 2 N cycles + small overhead | N cycles + small overhead
Float multiply-add pipeline | 4 stages | 6 stages
Idle power (when not in use or between vector operations) | Nearly zero (leakage only) | Same
Power while operating | (Small; we never measured it) | Probably similar

## Slide 16: Detailed improvements: Programming model
 | Hydra 3.3 | Hydra 4.2
Overall usability for firmware | Hard to use | Much easier to use
“HOCA_xxx” macro method | Ugly; used in most firmware | Only in compatibility mode
“Hydra assembler” method | Less ugly; in newer firmware | Only in compatibility mode
Easy function-style notation | No | Yes
Instruction opcodes | 16 bits wide | 32 bits wide
Instruction operands | Ad-hoc | Flexible vector-register model
Instruction buffering | 1 level + 1 partial level | 2 levels
CPU interrupts | 6 interrupt flags  1 CPU intr | 7 interrupt flags  1 CPU intr
Automatic handshaking to simplify register access by FW | No | Yes
Use by multi threads/tasks/cores | No | Yes
Error reporting | Basic | Detailed diagnostic info
Performance counter | No | Yes
Stored program unit | Hard to use | Flexible and easy to use

## Slide 17: Detailed improvements: Arithmetic
 | Hydra 3.3 | Hydra 4.2
Fully IEEE 754-compliant floating-point arithmetic | Not quite | Yes
Support for NaN values | No | Yes
Support for denorm values | No | Yes
Fused multiply-adds | No | Yes
Correctly rounded division | No | Yes
Support for half-precision | No | Yes
Fixed-point arithmetic | 16-bit only | 8-, 16-, and 32-bit
Mixed-format arithmetic | No | Yes
Packed K-bit floats | No | Yes (using Posits)
Square roots | Yes (not IEEE-rounded) | Same
Support for sin/cos/log/exp/… | No | Yes
Support for frexp/ldexp/… | No | Yes

## Slide 18: Detailed improvements: Memory addressing
 | Hydra 3.3 | Hydra 4.2
Linear/stride addressing | Yes | Yes
Scatter/gather indexing | Yes | Yes
Simple matrix addressing | Limited to 256 columns; tricky and confusing to use | Unlimited and easy to use
Transposed matrices | Limited | Flexible and general
General matrix row/col strides | No | Yes
Repeated-row/col matrices | No | Yes
Nested repeating patterns | No | Yes
Circular addressing | Very limited | Flexible and general
Bit-level data packing | Limited | Flexible and general
Pattern-mode source data | No | Yes
Memory scalar operands | No | Yes
Vector mask | Yes | More flexible, easier to use

## Slide 19: Detailed improvements: Special operations
 | Hydra 3.3 | Hydra 4.2
Fast Fourier Transforms (FFT) | Simple/basic | Faster and more flexible
Convolutions (1D and 2D) | Confusing and hard to use | Easier and more flexible
Matrix multiply | Yes | Easier and more flexible
Median filters (1D and 2D) | Optional | Yes
Basic min/max operations | Yes | Yes
Find local minima/maxima (accelerates IFP segmentation) | No | Yes
Row/column-wise min/max | No | Yes
Complex number arithmetic | No | Yes
Classify special float values | No | Yes
Integer log2 and variable shifts | No | Yes
Byte swap and bit reverse | No | Yes
Sorting/selection | Limited | Faster and more flexible
Block move or fill | Copy 32 bits per cycle | Copy 64 bits per cycle

## Slide 20: Detailed improvements: Neural networks/ML/AI
 | Hydra 3.3 | Hydra 4.2
Byte data types | No | Yes
BFLOAT16 data type | No | Yes
Posit data type | No | Yes
Byte-granular convolutions | No | Yes
SIMD operations on byte data | No | Yes (Hydra 4.2+)
Packed convolution weights | No | Yes
Packed sparse weights | No | Yes (limited)
Min/max convolutions | No | Yes
Simple minpool/maxpool | No | Yes
General pooling convolutions | No | (Planned; Hydra 4.2 omits it)
ReLU or ReLU6 in 1 instruction | Yes | Yes
Reasonably fast exp(x) | No | Yes
Other ML-inspired features | No | Ongoing development…

## Slide 21: Detailed improvements: Cryptographic features
 | Hydra 3.3 | Hydra 4.2
AES standard encrypt/decrypt | No | Yes (~10 cycles per byte)
AES/GCM carry-less multiply | No | Yes (~8 N2 cycles for CLMUL)
XXTEA encrypt/decrypt | No | Yes (~10 cycles per byte)
SHA-256/-224 standard hash | No | Yes (~5 cycles per byte)
CRC32/CRC16 hash | No | Yes (2 cycles per byte)
Pseudorandom numbers | No | Yes (½ cycle per byte)
RSA/DSA public-key arithmetic | Limited | Yes (N2 cycles to multiply two 32N-bit-wide integers)
Note: In areas such as Neural Networks and Cryptography, remember that Hydra is not trying to be as powerful as a big, expensive, dedicated NPU, GPU, or Crypto IP core
  It aims to deliver significantly better performance than pure firmware can do …
  … at modest, incremental hardware cost: Cheap enough to include it always “just in case”
  If we know we need (say) a big NPU, and our market justifies its cost, fine: We can get one that meets the need
  Hydra includes these features for a different reason: Cheaply looking ahead to meet speculative future needs
  This is important since our chips often live on for many years, eventually to be used in many products

## Slide 22: “Hydra Junior”
Hydra 4 can be built in a way that significantly reduces its area and cost, in return for a decrease in functionality
  `define HYDRA_JUNIOR
The Hydra Junior configuration removes features that are rarely used or not required for our basic touch firmware functionality:
  Slower FFTs, median filters, sorting, neural networks, and special math functions
  No cryptographic encryption or hashing; no random number generation
  No packed data, half-precision floats, or Posit data types
  No Stored Program Unit, multi-threaded operation, or Hydra 3 Compatibility Mode
  … and various other cost savings
Hydra 4 Junior is over 40% smaller than the full configuration of Hydra 4
  Full Hydra 4.2 is ~108K gates, and Hydra 4.2 Junior is ~61K gates, in TSMC 40nm EF
  (These are base synthesis numbers when not pushed for the fastest clock rate)
  We first used Hydra 4.1 Junior in the cost-reduced DIG2411 “Denmarke” chip

## Slide 23: “Hydra Junior”

## Slide 24: Hydra 4
Architecture overview
  Introduction
    What is it
    Why we need it
    Where it came from
  Using Hydra
  Hardware and implementation

## Slide 25: Refreshing Hydra 3
Hydra versions 1.0–3.3 have served us well in a variety of touch, display, and fingerprint chips at Synaptics
  Hydra is present in many of our most successful chips, but not in some of the highest-volume, lowest-cost chips
  This makes it hard to work out the total number of Hydras produced so far …
  … But most likely, well over a billion chips have shipped to date with some version of Hydra
Still, Hydra 3 was showing its age
Hydra 3.3 is still largely backward compatible to the original ten-year-old Hydra 1.0
  An architecture based on guesswork from days when our firmware was much less mature
  It was built around the 16-bit-centric architecture of older Chimera CPUs, which puts it out of step with modern CPUs including our own Chimera 4.2
 Time for a thorough refresh
Notes: Maybe a few billion by now…?

## Slide 26: Why refresh Hydra? (1)
Hydra is valuable: For example, Prometheus (and Triton) fingerprint matching
  Its image processing module runs 6x faster with Hydra 3 than it does in pure firmware on our Prometheus chip’s Tensilica Xtensa CPU
  … even though Prometheus has a maximally-configured >200K-gate 32-bit Xtensa at 192 MHz
   Match-in-sensor would not have been feasible without Hydra or something like it

## Slide 27: Why refresh Hydra? (2)
Hydra is valuable: For example, Prometheus (and Triton) fingerprint matching
Hydra is strategically valuable: For example, noise countermeasures in touch firmware
  With Hydra 2, we solved OLED display noise “in firmware” instead of with a one-year chip spin
    (Yes, I know, oversimplifying…)
  OLED display noise was not known yet, and our algorithms for it were not invented yet, back when we designed our DIG240x series chips with Hydra
  We had originally developed Hydra for something else
  We carried it forward into those chips “just in case” new tough problems might need more computational power
  That bet paid off when OLEDs came along
   A chip conceived and built with only enough strength for our pre-OLED firmware would never have had the horsepower to handle OLED displays

## Slide 28: Why refresh Hydra? (3)
Hydra is valuable: For example, Prometheus (and Triton) fingerprint matching
Hydra is still strategically valuable:
  Sure, future chips can (and should!) solve things like OLED noise in a more fundamental way
  Maybe they will have faster CPUs or better AFEs
  But without Hydra or something like it, we would have nothing left “in our back pocket” for the next OLED-like challenge
 And that is Synaptics’ bread and butter!
  Customers look to us because our technology has the strength and ingrained flexibility …
  … to “fix in firmware” with speed and agility …
  … even the toughest problems
Hydra is strategically valuable: For example, OLED touch firmware

## Slide 29: Why refresh Hydra? (4)
Hydra is valuable: For example, Prometheus (and Triton) fingerprint matching
Hydra is still strategically valuable:
Hydra is strategically valuable: For example, OLED touch firmware
Hydra is necessary
  Even our existing firmware is hard to run without it
  SiFive’s E76 is maxed out by Byrd’s needs
    … even though it is much larger than Chimera + Hydra combined
    Even if we can clock a CPU that fast, it is not clear we always should, from a power/noise/cost perspective
  Also, no affordable ARM processor can run as fast as E76
   We don’t know how to build an ARM-based touch controller that can run our full firmware unless we pair the ARM with Hydra or something like it
This was written with Cortex-M7 in mind; the newer Cortex-M52 might change that, but it is quite big and only questionably “affordable”!

## Slide 30: Why refresh Hydra? (5)
That’s all great, but Hydra 3 itself was getting old …
Our modern chips are 32-bit-oriented
  Synaptics’ Chimera and Hydra began as small 16-bit processors
  But Chimera 4.2 now supports 32-bit data, 32-bit addressing, and 32-bit interfaces to RAM (used today in DIG2405 / DIG2407 / DIG2408 “Vulcan” and “Keys”)
  Some customers want a 32-bit commercial CPU (e.g., one customer specified ARM Cortex-M4)
  Byrd and SmartBridge use a 32-bit RISC-V CPU, and future chips may use it too
Hydra 3 still has a 16-bit data path with 16-bit addressing and 16-bit RAM interfaces
   This is needlessly old-fashioned!
  Hydra 3 reads and writes floating-point numbers in two 16-bit halves, sequentially
    Its float operations run at half speed, even though our memories now support 32-bit-wide access
  Hydra 3’s 16-bit architecture has a hard time with > 64KW of RAM
  It is awkward to use when connected to modern 32-bit processors
  And it’s awkward to connect! It uses Chimera-specific buses; no AHB or APB

## Slide 31: Why refresh Hydra? (6)
Hydra 3 is too hard to use
Recent versions have made improvements, but it is still clumsy
  It is hard to construct the numeric “opcode”
  Parameters of the operation mingle in tricky ways
  Some parameters must be specified in multiple places
  Lots of sticky modes to watch out for; lots of restrictions to navigate
  Not a very “natural” interface to the firmware
  Meanwhile, we should be making Hydra easier and more accessible:
  Hydra’s best early power users are no longer here
One Hydra 3 VSUB instruction (in real IFP firmware) 

## Slide 32: Why refresh Hydra? (7)
Hydra 3 is hard to maintain
  The RTL was originally written by Kam Li in 2012 w/architectural guidance from Mark Pearce and me
  Hydra has evolved dramatically since then, but Hydra 3.3 is still built upon that old RTL
  Mark left Synaptics in 2014, and Kam left in 2017
  I took over Hydra, finished the work for Prometheus, and maintained and developed it since then
  I cultivated Cody Cziesler in Rochester to co-own Hydra; we lost him when RDC closed in 2018
  Today, I handle all of Hydra’s architecture, design, documentation, testing, and some tools by myself
  This is not “scalable”!
  So it would be great if Hydra’s internals were easy to teach and to work with; sadly …
Hydra 3 is hard to work with
  Its Verilog RTL is quirky and obscure “spaghetti code”: People find it impenetrable
  I took the time to learn it, but even I have a hard time implementing some feature requests
  It was getting hard to push Hydra 3 any further

## Slide 33: Why not just buy it?
Vector processors are an old idea — but getting popular again
However, even today’s “small” commercial vector processors are really big
  ARM recently released Cortex-M55 with “Helium / MVE” M-profile Vector Extension
  Yay! But …
Hydra 3 is less than 100K gates
  Similar in size to Chimera
  Together they are only as big as ARM M4 or SiFive RISC-V E34
SiFive’s E76 is quite a bit larger than ARM M4, and Hydra 4 is somewhat larger than Hydra 3
  But the principle is the same: Our chips are small; industry standard vector CPUs are not!
Chimera 4.2
Hydra 3.3
My idea of small!
(To be fair, ARM released a smaller Cortex-M52 since I wrote this in 2022)
Notes: It would be good to get analogous numbers for ARM’s Cortex-M52.

## Slide 34: Why not just buy it in RISC-V?
From a webinar on andestech.com
RISC-V offers a “V” vector extension
  An elegant state-of-the-art vector architecture
  Scalable in principle from “large” to “small” implementations
  But even its smallest configuration is still pretty big: 32×128-bit vector registers, etc.
Vendors like SiFive and Andes offer “V” mainly in their largest CPUs (> 1 million gates)
  With 512-bit-wide registers that can hold 16 floats at once
  And enough cache bandwidth to load or store 512 bits on every cycle
  And 16 floating-point multipliers and adders in a row, all operating in parallel
  Cool stuff, but way out of our league!
So, in today’s world, for our tiny chips, it still makes sense to build and develop Hydra

## Slide 35: Why not just buy it in RISC-V?
From a webinar on andestech.com
RISC-V offers a “V” vector extension
  An elegant state-of-the-art vector architecture
  Scalable in principle from “large” to “small” implementations
  But even its smallest configuration is still pretty big: 32×128-bit vector registers, etc.
Vendors like SiFive and Andes offer “V” mainly in their largest CPUs (> 1 million gates)
  With 512-bit-wide registers that can hold 16 floats at once
  And enough cache bandwidth to load or store 512 bits on every cycle
  And 16 floating-point multipliers and adders in a row, all operating in parallel
  Cool stuff, but way out of our league!
So, in today’s world, for our tiny chips, it still makes sense to build and develop Hydra
Since this slide was written, there are now some smaller CPUs available with the “V” extension in the 128-bit vector size, such as SiFive’s X160. But they are still quite large!
For example, “V”’s small-configured vector register file alone contains 32 x 128 = 4096 flip-flops, which is more flip-flops than in the entire Hydra 4.2 non-Junior core including all the registers, FIFOs, pipelines, arithmetic functions, address generators, controllers, etc., all together

## Slide 36
Big: RISC-V “V”, ARM Neon / SVE / MVE | Small: Hydra coprocessor
Many wide vector registers inside the CPU | Vector data resides in the main data RAM
Many ALUs / FPUs operating in parallel | Stream the data through one pipelined ALU / FPU
Vector Load + Vector Arithmetic + Vector Store are separate instructions | Multiple DMA channels load and store data in parallel with the ALU’s operation
To keep the ALUs busy, combine all these loads, arithmetic, and stores in superscalar fashion | The ALU is 100% utilized during large vector operations: No need for a big superscalar CPU
Without superscalar, a RAM-to-RAM vector multiply would need 4 cycles [load + load + multiply + store] to do (e.g.) 4 floating-point multiplications | Same net speed: One float multiplication per cycle For neural nets: Up to 4 SIMD byte MACs per cycle  3.2 GOPS at Byrd’s 400 MHz
V0 |  |  |  |  |  |  |  | 
V1 |  |  |  |  |  |  |  | 
V2 |  |  |  |  |  |  |  | 
V3 |  |  |  |  |  |  |  | 
V4 |  |  |  |  |  |  |  | 
V5 |  |  |  |  |  |  |  | 
V6 |  |  |  |  |  |  |  | 
⁝ |  |  |  |  |  |  |  | 
V30 |  |  |  |  |  |  |  | 
V31 |  |  |  |  |  |  |  | 
 | [0] | [1] | [2] | [3] | [4] | [5] | ∙∙∙ | [N-1]
128–1024 bits
…
vfmul.vv v30,v1,v3
vle32.v v1,(a2)
vse32.v v30,(t0)
Hydra 4.2
RISC-V Vector extension
ALUs

## Slide 37
Big: RISC-V “V”, ARM Neon / SVE / MVE | Small: Hydra coprocessor
Vectors need a lot of RAM bandwidth | Vectors still need a lot of RAM bandwidth!
RAM bandwidth comes from wide cache access: Read or write a whole cache line at a time | RAM bandwidth comes from multiple DMA channels connected to multiple interleaved banks of RAM
Big chips need a data cache anyway … | Small chips prefer to use tightly-coupled data RAM …
… so wide cache access is a natural fit | … and several small RAMs are faster than one big RAM, so we get our multiple-banked RAM for free
Scalable to almost arbitrarily huge systems | Optimized specifically for small “edge” systems
V0 |  |  |  |  |  |  |  | 
V1 |  |  |  |  |  |  |  | 
V2 |  |  |  |  |  |  |  | 
V3 |  |  |  |  |  |  |  | 
V4 |  |  |  |  |  |  |  | 
V5 |  |  |  |  |  |  |  | 
V6 |  |  |  |  |  |  |  | 
⁝ |  |  |  |  |  |  |  | 
V30 |  |  |  |  |  |  |  | 
V31 |  |  |  |  |  |  |  | 
 | [0] | [1] | [2] | [3] | [4] | [5] | ∙∙∙ | [N-1]
Load |  |  |  |  |  |  |  | 
Store |  |  |  |  |  |  |  | 
Data |  |  |  |  |  |  |  | 
cache |  |  |  |  |  |  |  | 
128–1024 bits
…
vfmul.vv v30,v1,v3
…
vle32.v v1,(a2)
vse32.v v30,(t0)
Hydra 4.2
RISC-V Vector extension
ALUs

## Slide 38: Hydra 4
Architecture overview
  Introduction
    What is it
    Why we need it
    Where it came from
  Using Hydra
  Hardware and implementation

## Slide 39: Hydra’s motivation and design
Why is a vector processor a good choice for us?
The next few slides tell the story behind Hydra’s development
  They are adapted from my earlier presentation, Hydra: A Supercomputer on Our Scale, which described Hydra 3
  Before we get into the details of Hydra 4, let’s see what motivated Hydra’s general architecture and approach
  The story goes back about 10 years, with echoes going much further back …

## Slide 40: Scalable computation
In 2012, large touch screens on laptops looked to be the Next Big Thing for Synaptics
They inspired us back then to develop Hydra version 1
Even though LTS did not become the big market we hoped …
… Hydra has proven effective, since then, for other compute-intensive tasks in our products
  In touch algorithms like OLED noise removal
  In fingerprint algorithms like Quantum Matcher
  And now, as smartphone screens and automotive screens get ever larger
  Recently: Hydra accelerates neural networks for state-of-the-art Accidental Contact Mitigation in our laptop touchpads and moisture immunity in our touchscreens for phones

## Slide 41: Scalable computation
What was so special about large touch screens?
Computationally, a large touch screen is like a small touch screen … but large!
  In every algorithm that scales with some “N”, N is larger
  N might be the number of row or column channels, or the number of touch pixels, max number of fingers, …
Also, our products were using more image processing and other advanced algorithms that crunch data in bulk
If N is 3x larger, you could just buy a 3x-faster CPU
  They exist, but they scale quickly in size and complexity
  More than 3x as big, expensive, and power-hungry
  For example, Byrd’s E76 is ~3x bigger than Chimera, but less than twice as fast (running real firmware)
 Is there a smarter answer than brute force?
Notes: See What Chimera Is All About for various E76/Chimera size and performance comparisons.

## Slide 42: Scaling with N: Vector processors
A vector processor is a computer that works on numbers N-at-a-time
On a traditional general-purpose processor, each instruction does one “thing” at a time:
ADD a, b, c // Set a ← b + c (using a hypothetical example processor…)
Such processors are called scalar processors
  (Borrowing the mathematical term for “a single number” instead of a vector or matrix)
Some processors can do several scalar operations at once, as if one larger operation:
ADD a, b, c // Set a ← b + c LOAD i, 0 // Set i ← 0
This is still scalar, not vector, because it is programmed in terms of scalar operations
  Instead, it is called superscalar
  See our Chimera for a simple example, and SiFive’s E76 for a larger-scale example
  See big x86 and ARM Cortex-A processors for really ambitious examples
Both together in one clock cycle

## Slide 43: Scaling with N: Vector processors
When a scalar processor works on a vector, doing the same thing to a whole array of N numbers, it must use a loop of scalar instructions:
LOAD i, 0 // Start with i ← 0 (again using a hypothetical processor!) again: LOAD B[i] // Load the next two input vector elements … ADD C[i] // … and compute their sum STORE A[i] // Set A[i] ← B[i] + C[i] ADD i, 1 // Increase i ← i + 1 BLT i, N, again // Branch if i < N back to do it again
A vector processor expresses the whole thing as one instruction:
VADD VL(N) A, B, C // Set A[i] ← B[i] + C[i] for all i = 0 … N−1
It may be a slow instruction, internally taking many steps to work through a big vector …
… but it is still much better than a loop of 5N instructions!

## Slide 44: Mixing vector and scalar processing
Vector processors are efficient when your program is composed all of vector operations such as “add vector B to vector C”
Real programs are not like that:
  Our touch and fingerprint firmware sometimes operates on N channels or N pixels in bulk
  … but other times, it does lots of individual “this-and-that” operations on scalar data
So, in reality, we can’t replace our general-purpose scalar processor with a vector processor
Instead: Combine the two!

## Slide 45: Mixing vector and scalar processing
Two ways to combine vector + scalar:
  Make a processor that can do both scalar instructions and vector instructions
  Or augment a general-purpose processor with a vector “co-processor” to help with heavy math
For the T1326 “Oahu” touch controller (circa 2012), we decided to add a vector coprocessor to sit alongside our traditional Chimera processor
This became Hydra 1.0
  Implemented by Kam Li; architected by Mark Pearce and Dave G.
Scalar
Vector
Scalar
Vector

## Slide 46: A legendary example
What kind of vector coprocessor should we use?
  Off-the-shelf vector processors were far too “big” for touch controllers (still true today, c. 2022!)
  So, in true Synaptics style, we built our own vector coprocessor to suit our needs
What kinds of operations should it support?
Can we just recast our firmware’s algorithms in the form of specialized hardware?
  No: Our firmware evolves way too fast for that
  And the firmware varies too much, adapting to the needs of each customer and project
Instead, we wanted a reasonably general-purpose, flexible vector architecture
  What does that look like?
For a model, we looked to the most famous vector computer of all …

## Slide 47
The Cray-1 supercomputer
Notes: Photo is “The Original Cray 1 Supercomputer, at AT&T Bell Labs circa 1977”, not sure where I found it.

## Slide 48: Seymour Cray’s heritage
The Cray-1’s designer, Seymour Cray, first made his name with the CDC-6600 supercomputer
When it came out in 1964, the CDC-6600 was 3x faster than its fastest competitor
It remained the world’s fastest computer until 1969 [Wikipedia]

## Slide 49: Cray’s innovations
How did Cray achieve such a huge jump in performance?
 Design innovation!
He rethought everything about computer architecture and design
For example:
The CDC-6600 pioneered the “load/store” organization that paved the way for all modern RISC processor architectures
This idea is still widely used today
In fact, our Chimera is a rare bird for not using it
  Why? See my talk, “What Chimera is All About”
CDC-6600 reference manual
Notes: The Chimera slide deck will be available soon on github.com/synaptics-chimera.

## Slide 50: Cray’s innovations
For another example:
The CDC-6600 could keep multiple instructions running simultaneously, one in each functional unit
 Superscalar execution
This idea, too, was pioneered by Cray and is still widely used today
(… including, in a simple form, in our own Chimera processor!)

## Slide 51: Cray’s innovations: One more example

## Slide 52: Cray’s innovations: One more example
To let the fast main processor focus on the main task …
The CDC-6600 had a separate peripheral processor to manage real‐time hardware functions
Each of 10 peripherals gets its own “virtual” control processor, dedicated to the peripheral
A single hardware processor simulates 10 independent processors by time-slicing
It performs one instruction at a time from each virtual processor in round-robin fashion

## Slide 53: Cray’s innovations: One more example
In other words: The CDC-6600 had hardware multithreading!
Interleaved hardware threads are not so common in today’s computers
But if you work at Synaptics, the idea might sound familiar!
Chimera uses threads for the same reason: Efficiently dividing its time among many real-time tasks
Seymour Cray’s innovations have quietly guided us all along

## Slide 54: Another Cray hallmark
Cray designed his machines by hand, with a small, focused team
The head of IBM asked how Cray could so badly beat IBM’s “vast development activities” with “only 34 people, including the janitor”
Cray: “It seems like Mr. Watson has answered his own question”
We follow Cray’s lead in this, too
  Chimera’s hardware team has varied in size, sometimes as “vast” as 4 or 5 people, sometimes just me alone
  Hydra 1.0 was architected by Mark Pierce, Kam Li, and me; and Kam (and later I) did the whole implementation solo
  A small team can (and must!) focus to succeed
Notes: The legendary “Janitor Memo”, and several other images here, came from www.computerhistory.org.

## Slide 55: Another Cray hallmark
Cray designed his machines by hand, with a small, focused team
The head of IBM asked how Cray could so badly beat IBM’s “vast development activities” with “only 34 people, including the janitor”
Cray: “It seems like Mr. Watson has answered his own question”
We follow Cray’s lead in this, too
  Chimera’s hardware team has varied in size, sometimes as “vast” as 4 or 5 people, sometimes just me alone
  Hydra 1.0 was architected by Mark Pierce, Kam Li, and me; and Kam (and later I) did the whole implementation solo
  A small team can (and must!) focus to succeed
A related, wonderful (maybe apocryphal?) story:
Jobs to Cray: We used your Cray-1 to design the Mac!
Cray’s reply: Funny, I’m designing the Cray-3 on a Mac!

## Slide 56: The Cray-1
For his next computer, Cray looked for the next huge leap in performance
He observed that scientific computations often involve arithmetic on large vectors and matrices
Why not build a computer that’s actually meant for that kind of computation?
for (i = 0; i < N; i++) A[i] = B[i] + C[i]; VADD A, B, C
B[0] | B[1] | B[2] | B[3] | B[4] | B[5] | B[6] | B[7] | ∙∙∙ | B[N-1]
+ | + | + | + | + | + | + | + |  | +
C[0] | C[1] | C[2] | C[3] | C[4] | C[5] | C[6] | C[7] | ∙∙∙ | C[N-1]
↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ |  | ↓
A[0] | A[1] | A[2] | A[3] | A[4] | A[5] | A[6] | A[7] | ∙∙∙ | A[N-1]

## Slide 57: The Cray-1
Cray-1, introduced in 1976, once again held the speed record for years
As usual, it was packed with innovations at every level
Not just the vector instruction set
But even the physical design
  Its distinctive round shape was not just for show: It optimized routing of wires
  Wires were all cut to the same length so that the speed-of-light delays through them were balanced!
Cray-1 reference manual

## Slide 58: The Cray-1 is now history
Literally: You can find it and other Cray machines at the Computer History Museum in Mountain View, California
Cray-1’s are still used today …
… but only as stylish furniture
  Actually those are power / cooling units, but anyway …
Vector machines in general fell out of fashion
  Most computer architectures have “SIMD” instructions instead, which are like vector instructions but with small fixed N = 2 or 4
  The open-source RISC-V processor architecture has an excellent vector extension that is gaining traction (and whose designers also cite Cray as inspiration)
Cray’s vector approach lives on today in Hydra
(Google images)

## Slide 59: Ancient history?
Here we are, a quarter or so into the 21st century
Why care about antique machines like the CDC-6600 or the Cray-1?
  Apple’s M1 Ultra chip (c. 2022) has 114 billion transistors — wow!
  So why are our chips stuck in the unfashionable 1970’s?
  Why study such dinosaurs when they are so totally outclassed by modern technology?
The touch controllers we build today can afford a few million transistors at most
  The M1 Ultra’s innovations, impressive as they are …
  … and fun as they are to learn about …
  … are irrelevant to what we do here
  Many orders of magnitude bigger than we could dream of in our tiny mixed-signal embedded-Flash high-voltage silicon

## Slide 60: Ancient history
The largest discrete touch chip we have ever built, DIG2409 “Byrd”, has roughly ½ million gates of digital logic
  How many gates of logic did the Cray-1 have?
   About the same!
  The Cray-1 may have filled a room, but in the most important way, it was “about as big” as Byrd
This was an era when the best computer designers in the world …
  … with enormous resources on tap, a “blank check” from their customers …
  … overcoming the severe technological limitations of their day …
  … were building top-performing computers on our current budget of complexity
For us, the Cray-1, not the M1, is the model of greatness that makes the most sense to study and aspire to
Cray-1 reference manual

## Slide 61: Vector processors
A vector processor offers single instructions for various common operations on vectors
  VADD A, B, C // Add two vectors: A[i] ← B[i] + C[i] (for all 0 ≤ i < N)
  VMADD A, B, C, D // Multiply-add: A[i] ← B[i] + (C[i] * D[i])
  VMAC sum, B, C // Multiply-accumulate: sum ← (B[0] * C[0]) + (B[1] * C[1]) + ∙∙∙
  VMOVG A, B, C // Move-and-gather: A[i] ← B[C[i]]
  … and so on
If N = 4 (say), we could just build 4 arithmetic units that work in parallel, all at once
  This is the approach taken by, e.g., x86 SSE/AVX; ARM Cortex-M4 SIMD; Cortex-A with Neon
But in general, we can’t afford to do an N-element vector operation all in one clock cycle
  Not when N gets large
  Especially not when N is large and variable!
Instead, Hydra works sequentially, but very efficiently, using a deep pipeline

## Slide 62: Pipelined processing
Computers go fast by breaking a complex operation into several small steps
Each step does a self-contained piece of the job
These self-contained steps can be overlapped in assembly-line fashion
A “pipeline” of steps
This is much more efficient than finishing each whole operation before starting the next
Detroit Historical Society
Notes: Postcard image is from the Detroit Historical Society website (which grants free permission to reproduce)

## Slide 63: Deep pipelines
Long computer pipelines, with many steps, get complicated very quickly!
There are countless potential interactions among all the instructions in the various stages
This makes them either …
  … inefficient, as the pipeline often stalls to resolve the interactions …
  … or very hard to program, due to the instruction rearrangement needed to avoid stalling …
  … or painfully big and complicated, due to the extensive hazard detection, data forwarding, speculative execution, dynamic instruction reordering, and branch prediction needed to eliminate stalls at the hardware level
“Billion transistor” CPUs can efficiently use deep pipelines
  The Intel chip in your laptop might have a 20-stage pipeline!
But general-purpose CPUs in our price range cannot
  This is why low-cost microcontrollers have short pipelines
  And, in turn, it’s why small micros can’t clock nearly as fast as big application processors
ARM Cortex-M7 8-stage pipeline

## Slide 64: Pipelined vector processors
But for a vector processor, deep pipelines are [relatively] easy!
Consecutive operations are predictable
The stages can’t possibly interact: Each stage is working on a different vector element
Fetch B | B[0] | B[1] | B[2] | B[3] | B[4] | B[5] | B[6] | B[7] | B[8] | B[9] |  |  |  | 
Fetch C |  | C[0] | C[1] | C[2] | C[3] | C[4] | C[5] | C[6] | C[7] | C[8] | C[9] |  |  | 
Exec (1) |  |  | [0] | [1] | [2] | [3] | [4] | [5] | [6] | [7] | [8] | [9] |  | 
Exec (2) |  |  |  | [0] | [1] | [2] | [3] | [4] | [5] | [6] | [7] | [8] | [9] | 
Write A |  |  |  |  | A[0] | A[1] | A[2] | A[3] | A[4] | A[5] | A[6] | A[7] | A[8] | A[9]
B[0] | B[1] | B[2] | B[3] | B[4] | B[5] | B[6] | B[7] | B[8] | B[9]
+ | + | + | + | + | + | + | + | + | +
C[0] | C[1] | C[2] | C[3] | C[4] | C[5] | C[6] | C[7] | C[8] | C[9]
↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓
A[0] | A[1] | A[2] | A[3] | A[4] | A[5] | A[6] | A[7] | A[8] | A[9]
(Hydra’s actual pipeline is deeper than shown here)

## Slide 65: Getting the data in and out
Vector processors need lots of bandwidth to vector memory
During this vector operation, every cycle reads two numbers and writes a third number
How is this possible?
  One answer: Keep “A”, “B”, and “C” in separate memories
  The Cray-1 did this by holding vector data in eight “vector registers” built as 8 independent 64-entry RAMs (today, RISC-V “V” works similarly)
  Traditional DSPs do this by forcing people to manually allocate different vectors in different sections of main RAM (“X memory” vs. “Y memory”); then the DSP can access X RAM and Y RAM at once via two parallel ports
Fetch B | B[0] | B[1] | B[2] | B[3] | B[4] | B[5] | B[6] | B[7] | B[8] | B[9] |  |  |  | 
Fetch C |  | C[0] | C[1] | C[2] | C[3] | C[4] | C[5] | C[6] | C[7] | C[8] | C[9] |  |  | 
Exec (1) |  |  | [0] | [1] | [2] | [3] | [4] | [5] | [6] | [7] | [8] | [9] |  | 
Exec (2) |  |  |  | [0] | [1] | [2] | [3] | [4] | [5] | [6] | [7] | [8] | [9] | 
Write A |  |  |  |  | A[0] | A[1] | A[2] | A[3] | A[4] | A[5] | A[6] | A[7] | A[8] | A[9]

## Slide 66: Banked data RAM
Another answer: Suppose we structure RAM as (say) 8 interleaved banks
The data word at memory word address X is stored in bank (X % 8) at offset (X / 8) within the bank
Notice that “fetch B”, “fetch C”, and “write A” always use different banks!
The vector engine can operate at full speed on vectors directly in RAM
  If the vectors are aligned in memory in a favorable way
  See later for how Hydra deals well with unfavorably/randomly aligned data
Some early vector machines used interleaved RAM (CDC STAR; Cray-1), and we use this approach in Hydra
Fetch B | B[0] | B[1] | B[2] | B[3] | B[4] | B[5] | B[6] | B[7] | B[8] | B[9] |  |  |  | 
Fetch C |  | C[0] | C[1] | C[2] | C[3] | C[4] | C[5] | C[6] | C[7] | C[8] | C[9] |  |  | 
Exec (1) |  |  | [0] | [1] | [2] | [3] | [4] | [5] | [6] | [7] | [8] | [9] |  | 
Exec (2) |  |  |  | [0] | [1] | [2] | [3] | [4] | [5] | [6] | [7] | [8] | [9] | 
Write A |  |  |  |  | A[0] | A[1] | A[2] | A[3] | A[4] | A[5] | A[6] | A[7] | A[8] | A[9]
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0000 |  |  |  |  |  |  |  | 
0001 |  |  |  |  |  |  |  | 
0002 |  |  |  |  |  |  |  | 
0003 |  |  |  |  |  |  |  | 
0004 |  |  |  |  |  |  |  | 
0005 |  |  |  |  |  |  |  | 
0006 |  |  |  |  |  |  |  | 
0007 |  |  |  |  |  |  |  | 
0008 |  |  |  |  |  |  |  | 
0009 |  |  |  |  |  |  |  | 
000A |  |  |  |  |  |  |  | 
000B |  |  |  |  |  |  |  | 
000C |  |  |  |  |  |  |  | 
000D |  |  |  |  |  |  |  | 
000E |  |  |  |  |  |  |  | 
000F |  |  |  |  |  |  |  | 
0010 |  |  |  |  |  |  |  | 
0011 |  |  |  |  |  |  |  | 
0012 |  |  |  |  |  |  |  | 
0013 |  |  |  |  |  |  |  | 
0014 |  |  |  |  |  |  |  | 
0015 |  |  |  |  |  |  |  | 
0016 |  |  |  |  |  |  |  | 
0017 |  |  |  |  |  |  |  | 
0018 |  |  |  |  |  |  |  | 
0019 |  |  |  |  |  |  |  | 
001A |  |  |  |  |  |  |  | 
001B |  |  |  |  |  |  |  | 
001C |  |  |  |  |  |  |  | 
001D |  |  |  |  |  |  |  | 
001E |  |  |  |  |  |  |  | 
001F |  |  |  |  |  |  |  | 
0020 |  |  |  |  |  |  |  | 

## Slide 67: Hydra’s pipeline
Here are some actual timing diagrams from the Hydra 4 User’s Guide (based on chip simulation traces)
First, a VADD operation on a chip with Hydra 4.2 and four banks of RAM 
This VMADD (fused multiply-add) accesses four vectors at once in four banks 
  Here, Hydra’s channel FIFO buffers absorb some stalls that occur due to the vectors’ alignment in RAM (see the “Hardware” section later)

## Slide 68: The Hydra 4 vector coprocessor
The rest of this presentation introduces Hydra 4, Synaptics’ latest vector coprocessor
  First silicon in the SB7900A0 “SmartBridge” chip in early 2023
  Also appearing in DIG2409 “Byrd” in 2024 and DIG2411 “Denmarke” in 2025
  Hydra 4.2 is due to appear first in DIG2409B in 2026
  Probably next in the B1458 “Atlas” match-in-sensor fingerprint chip
Leveraging the success of Hydra 3 while improving every detail
Drawing upon the rich heritage of vector processors established by Cray

## Slide 69
Iolaos and Heracles battling the Hydra
Etruscan vase based on a Greek painting, circa 520 BC
(Legion of Honor Museum, San Francisco)
Heracles preparing to attack the Hydra
Greek jar made in Athens, circa 480 BC
(British Museum, London)
Notes: (I took these photos myself during visits to these museums.)

## Slide 70: Hydra 4
Architecture overview
  Introduction
  Using Hydra
    Examples
    Hydra registers
    Vector instructions
    Data types
    Addressing modes
    Stored program unit
    Documentation and tools
    Hydra 4.2 functionality
    Performance
  Hardware and implementation

## Slide 71: Hydra 4
Architecture overview
  Introduction
  Using Hydra
    Examples
    Hydra registers
    Vector instructions
    Data types
    Addressing modes
    Stored program unit
    Documentation and tools
    Hydra 4.2 functionality
    Performance
  Hardware and implementation

## Slide 72: Using Hydra 4: A simple example
Hydra 4’s header file defines functions and macros for invoking Hydra in a C program:
Here, the hydra_vadd() function tells Hydra to begin a VADD operation with the indicated vector operands and vector length
  Hydra reads 100 short integers from the elements of the array data[] …
  … and it reads 100 long integers from every 5th element of the array inputs[]; …
  … it adds them together to get 100 sums, …
  … and then it stores these sums, as long integers, in results[]
Equivalent to…
for (i = 0; i < 100; i++)
results[i] = data[i] + inputs[5*i];
#include "hydra4_defs.h"
long results[100], inputs[500];
short data[100];
hydra_vadd(hydra_set_vl(100),
hydra_vector(results, HYDRA_INT32),
hydra_vector(data, HYDRA_INT16),
hydra_strided(inputs, HYDRA_INT32, 5));
Notes: This C code is not quite equivalent to this Hydra operation, because the Hydra operation will saturate the result in case of a 32-bit integer overflow, while typical C compilers discard the high bits upon an overflow. Hydra’s “truncating integer” types more precisely model how C integer arithmetic works: See later in this presentation.

## Slide 73: Sequential instructions
The result of a Hydra vector operation can feed directly into the next operation:
These operations automatically overlap inside Hydra as much as possible
  The hydra_vadd() function starts Hydra working on the VADD and then returns immediately
  The hydra_vmul() then sets up the VMUL operation while the VADD crunches away inside Hydra
  The VMUL waits in Hydra’s instruction buffer, then immediately runs as soon as VADD completes
Equivalent to…
for (i = 0; i < 100; i++)
results[i] = data[i] + inputs[5*i];
for (i = 0; i < 100; i++)
results[i] *= scales[i];
#include "hydra4_defs.h"
long results[100], inputs[500];
short data[100], scales[100];
hydra_vadd(hydra_set_vl(100),
hydra_vector(results, HYDRA_INT32),
hydra_vector(data, HYDRA_INT16),
hydra_strided(inputs, HYDRA_INT32, 5));
hydra_vmul(0, // No need to set VL again if it is unchanged.
hydra_vector(results, HYDRA_INT32),
_, // Shorthand for “same vector as the result vector.”
hydra_vector(scales, HYDRA_INT16));
… which computes this…
for (i = 0; i < 100; i++)
results[i] = ((data[i] + inputs[5*i]) *
scales[i]);

## Slide 74: Reading Hydra’s results in firmware
When firmware wishes to look directly at Hydra’s results, it must wait for Hydra to finish:
Simulating with HydraSim will catch the error if you forget to call hydra_wait()
There is a convenient notation to run a Hydra operation and wait for it to complete:
Equivalent to…
for (i = 0; i < 100; i++)
results[i] = data[i] + inputs[5*i];
for (i = 0; i < 100; i++)
results[i] *= scales[i];
some_stuff(results[0] + results[99]);
#include "hydra4_defs.h"
long results[100], inputs[500];
short data[100], scales[100];
hydra_vadd(hydra_set_vl(100),
hydra_vector(results, HYDRA_INT32),
hydra_vector(data, HYDRA_INT16),
hydra_strided(inputs, HYDRA_INT32, 5));
hydra_vmul(0, // No need to set VL again if it is unchanged.
hydra_vector(results, HYDRA_INT32),
_, // Shorthand for “same vector as the result vector.”
hydra_vector(scales, HYDRA_INT16));
hydra_wait();
some_stuff(results[0] + results[99]);
hydra_vmul_w(…); … is the same as … hydra_vmul(…); hydra_wait();

## Slide 75: Combining data types
Operations like hydra_vadd() can work with any combination of data types:
Hydra performs the necessary type conversions on its inputs and outputs as it goes:
  For each index i from 0 up to the vector length …
  Hydra reads the i’th set of input values from RAM (here, they are data[i] and inputs[i]);
  It interprets each input value as an exact mathematical number, according to its data type;
  It internally calculates the exact mathematical result;
  Then it rounds, saturates, and converts the exact result to match the output data type;
  And finally, it stores the i’th result back to RAM (here, the result goes in results[i])
#include "hydra4_defs.h"
float results[100]; // Single-precision floating-point numbers.
long data[100]; // Signed 32-bit fixed-point numbers with 22 integer bits and 10 fraction bits.
unsigned short inputs[500]; // Unsigned 16-bit integers.
hydra_vadd(hydra_set_vl(100),
hydra_vector(results, HYDRA_FLOAT),
hydra_vector(data, HYDRA_FIX32(10)),
hydra_strided(inputs, HYDRA_UINT16, 5));

## Slide 76: Combining addressing modes
Also, operations like hydra_vadd() work with any combination of addressing modes:
Each mode defines how each index i = 0, 1, …, VL−1 maps to a memory address:
  For simple linear vectors: base_address + (i * element_size)
  For strided vectors: base_address + (i * stride * element_size)
  For a repeated-row matrix: base_address + ((i % width) * element_size)
  For a general matrix: base_address + ((((i / width) * row_stride) + ((i % width) * column_stride)) * element_size)
  … and so on, with many supported addressing modes
#include "hydra4_defs.h"
float results[5][20]; // Single-precision floating-point numbers.
long data[20][5]; // Signed 32-bit fixed-point numbers with 22 integer bits and 10 fraction bits.
unsigned short inputs[20]; // Unsigned 16-bit integers.
hydra_vadd(hydra_set_vl(5*20),
hydra_matrix(results, HYDRA_FLOAT, 20), // A 5x20 matrix.
hydra_tmatrix(data, HYDRA_FIX32(10), 5), // A 5x20 transposed view of a 20x5 matrix in RAM.
hydra_rrmatrix(inputs, HYDRA_UINT16, 20)); // A 20-element row repeated to form a 5x20 matrix.

## Slide 77: Scalar values
Sometimes, an input to a vector operation will be the same for every vector element
  These are called “scalar values”
  Hydra 4 can take a scalar value directly, or it can draw a scalar value from a RAM location:
Hydra can also generate various numeric patterns as inputs:
float my_data[100];
float my_factor;
hydra_vmul(hydra_set_vl(100), // my_data[i] *= 3.1415 for all i.
hydra_vector(my_data, HYDRA_FLOAT), _,
hydra_scalar_float(3.1415));
hydra_vmul(hydra_set_vl(100), // my_data[i] *= my_factor for all i.
hydra_vector(my_data, HYDRA_FLOAT), _,
hydra_mscalar(&my_factor, HYDRA_FLOAT)); // “mscalar” = “memory scalar”.
hydra_vmul(hydra_set_vl(100), // my_data[i] *= (10+2*i) for all i.
hydra_vector(my_data, HYDRA_FLOAT), _,
hydra_pattern(10, 2));

## Slide 78: Vector masks
Operations can apply conditionally to selected vector elements
  First, an operation such as vector comparison creates a vector mask with one bit per element
  Subsequent operations can be made to apply only if the mask bit is 1, or only if the mask bit is 0
float my_data[100];
uint32_t my_mask[HYDRA_VM_SIZE(100)]; // == [4], since 4*32 ≥ 100 bits.
hydra_vcmp_gt(hydra_set_vl(100), // my_mask[bit i] = (my_data[i] > 3.1415) ? 1 : 0.
hydra_mask_gen(my_mask),
hydra_vector(my_data, HYDRA_FLOAT),
hydra_scalar_float(3.1415));
hydra_vmul(hydra_mask_if(my_mask), // if (my_mask[bit i] == 1) my_data[i] *= 0.5.
hydra_vector(my_data, HYDRA_FLOAT), _,
hydra_scalar_float(0.5));
hydra_vmov(hydra_mask_else(my_mask), // if (my_mask[bit i] == 0) my_data[i] = −1.
hydra_vector(my_data, HYDRA_FLOAT),
hydra_scalar_float(-1.0));

## Slide 79: How Hydra functions interface to the hardware
The functions hydra_vadd(), hydra_vector() , hydra_strided(), etc., …
HYDRA_P->VL = 100;
HYDRA_P->V0CFG = 0x00000020;
HYDRA_P->V0ADDR = (int) results;
HYDRA_P->V1CFG = 0x00000010;
HYDRA_P->V1ADDR = (int) data;
HYDRA_P->V2CFG = 0x00005220;
HYDRA_P->V2ADDR = (int) inputs;
while (!(HYDRA_P->IRQ & 2)) { }
HYDRA_P->OPCODE = 0x00006210;
Equivalent to…
for (i = 0; i < 100; i++)
results[i] = data[i] + inputs[5*i];
#include "hydra4_defs.h"
long results[100], inputs[500];
short data[100];
hydra_vadd(hydra_set_vl(100),
hydra_vector(results, HYDRA_INT32),
hydra_vector(data, HYDRA_INT16),
hydra_strided(inputs, HYDRA_INT32, 5));
hydra_set_vl(100);
hydra_set_vector(HYDRA_V0, results, HYDRA_INT32);
hydra_set_vector(HYDRA_V1, data, HYDRA_INT16);
hydra_set_strided(HYDRA_V2, inputs, HYDRA_INT32, 5);
hydra_vadd(0, HYDRA_V0, HYDRA_V1, HYDRA_V2);
… expand to a sequence of lower-level operations:
… which, in turn, translate to accessing various Hydra hardware registers:

## Slide 80: Vector registers
Like many vector machines, Hydra 4 organizes vector data as a set of vector registers
  Large vector processors such as Cray, ARM Neon, and RISC-V “V” have a large set of vector registers that directly store the vector data inside the CPU
  To save cost, Hydra instead stores the contents of each vector in the chip’s main data RAM
  Hydra’s vector registers V0–V7 are just descriptors that indicate the data type, addressing mode (the RAM access pattern), and base address of the data in RAM
  Functions such as hydra_set_strided() simply initialize a Vn register with that information:
  Internally, this corresponds to writing to a pair of Hydra registers called VnCFG and VnADDR (for some n = 0 … 7)
HYDRA_P->VL = 100;
HYDRA_P->V0CFG = 0x00000020;
HYDRA_P->V0ADDR = (int) results;
HYDRA_P->V1CFG = 0x00000010;
HYDRA_P->V1ADDR = (int) data;
HYDRA_P->V2CFG = 0x00005220;
HYDRA_P->V2ADDR = (int) inputs;
while (!(HYDRA_P->IRQ & 2)) { }
HYDRA_P->OPCODE = 0x00006210;
hydra_set_vl(100);
hydra_set_vector(HYDRA_V0, results, HYDRA_INT32);
hydra_set_vector(HYDRA_V1, data, HYDRA_INT16);
hydra_set_strided(HYDRA_V2, inputs, HYDRA_INT32, 5);
hydra_vadd(0, HYDRA_V0, HYDRA_V1, HYDRA_V2);
HYDRA_P->VL = 100;
HYDRA_P->V0CFG = 0x00000020;
HYDRA_P->V0ADDR = (int) results;
HYDRA_P->V1CFG = 0x00000010;
HYDRA_P->V1ADDR = (int) data;
HYDRA_P->V2CFG = 0x00005220;
HYDRA_P->V2ADDR = (int) inputs;
while (!(HYDRA_P->IRQ & 2)) { }
HYDRA_P->OPCODE = 0x00006210;
hydra_set_vl(100);
hydra_set_vector(HYDRA_V0, results, HYDRA_INT32);
hydra_set_vector(HYDRA_V1, data, HYDRA_INT16);
hydra_set_strided(HYDRA_V2, inputs, HYDRA_INT32, 5);
hydra_vadd(0, HYDRA_V0, HYDRA_V1, HYDRA_V2);

## Slide 81: Choosing the vector registers
Handy functions such as hydra_strided() automatically select the next free Vn:
  The function then invokes hydra_set_strided() to initialize the selected vector Vn
  It returns a constant such as HYDRA_V2, suitable for passing to the function hydra_vadd()
  hydra_vadd() formats the vector numbers into the appropriate bits of the Hydra instruction opcode, combined with bits that select the instruction itself and some optional “modifier” bits
  It posts this opcode to the OPCODE register to start Hydra
#include "hydra4_defs.h"
long results[100], inputs[500];
short data[100];
hydra_vadd(hydra_set_vl(100),
hydra_vector(results, HYDRA_INT32),
hydra_vector(data, HYDRA_INT16),
hydra_strided(inputs, HYDRA_INT32, 5));
HYDRA_P->VL = 100;
HYDRA_P->V0CFG = 0x00000020;
HYDRA_P->V0ADDR = (int) results;
HYDRA_P->V1CFG = 0x00000010;
HYDRA_P->V1ADDR = (int) data;
HYDRA_P->V2CFG = 0x00005220;
HYDRA_P->V2ADDR = (int) inputs;
while (!(HYDRA_P->IRQ & 2)) { }
HYDRA_P->OPCODE = 0x00006210;
…
hydra_set_strided(HYDRA_V2, inputs, HYDRA_INT32, 5);
hydra_vadd(0, HYDRA_V0, HYDRA_V1, HYDRA_V2);

## Slide 82: Using interrupts
Hydra can be set to send an interrupt signal to the host CPU on various conditions:
  Interrupt when Hydra is READY to receive another instruction
  Interrupt when Hydra is IDLE: All posted instructions are done
    Waiting for an IDLE interrupt is like calling hydra_wait()
  Interrupt when an ERROR occurs, etc.…
  Hydra’s IEN register controls which events, if any, will signal an interrupt
On traditional RISC CPUs, interrupts have tens or hundreds of cycles of overhead
  It is not practical to use interrupts to wait for Hydra in normal circumstances
  Therefore, the standard Hydra functions do not use interrupts by default when building for RISC-V or ARM
  Instead, they use spin loops to wait for READY or IDLE 
  But interrupts are available for very long waits, e.g., waiting for a big matrix-multiply or SPU program to finish
HYDRA_P->VL = 100;
HYDRA_P->V0CFG = 0x00000020;
HYDRA_P->V0ADDR = (int) results;
HYDRA_P->V1CFG = 0x00000010;
HYDRA_P->V1ADDR = (int) data;
HYDRA_P->V2CFG = 0x00005220;
HYDRA_P->V2ADDR = (int) inputs;
while (!(HYDRA_P->IRQ & 2)) { }
HYDRA_P->OPCODE = 0x00006210;
while (!(HYDRA_P->IRQ & 1)) { }
hydra_vadd_w(…)

## Slide 83: Using interrupts on Chimera
Chimera’s interrupts are very fast and lightweight
  When building for Chimera, the same Hydra functions generate code that puts the thread to sleep, waiting for an interrupt
  These functions wait for the READY interrupt before posting an instruction to Hydra
    In the common case that Hydra was READY already, the interrupt is already asserted
    Chimera does not sleep, and no time is wasted
  … and they wait for the IDLE interrupt to implement hydra_wait(), hydra_vadd_w(), etc.
  Other firmware threads can run during that time
    Or the CPU can sleep, conserving power
  Here, the BSET- or BCLR-to-IEN instruction takes just one Chimera clock cycle 
  … and the SLEEP instruction also takes one cycle
HYDRA_P->VL = 100;
HYDRA_P->V0CFG = 0x00000020;
HYDRA_P->V0ADDR = (int) results;
HYDRA_P->V1CFG = 0x00000010;
HYDRA_P->V1ADDR = (int) data;
HYDRA_P->V2CFG = 0x00005220;
HYDRA_P->V2ADDR = (int) inputs;
while (!(HYDRA_P->IRQ & 2)) { }
HYDRA_P->OPCODE = 0x00006210; while (!(HYDRA_P->IRQ & 1)) { }
HYDRA_P->IEN |= 2; SLEEP();
HYDRA_P->IEN &= ~2; SLEEP();
hydra_vadd_w(…)

## Slide 84: Eliminating setup overhead
Doesn’t it take time to write to all those Hydra hardware registers for every instruction?
  Actually, no!
  During a sequence of Hydra instructions, the next instruction is always pending in the instruction buffer
  The time spent writing to registers, etc., completely overlaps the vector operations running inside Hydra
  Hydra stays busy 100% of the time (if N is large)

## Slide 85: Instruction buffer
Hydra’s two-stage instruction buffer can hold one executing vector instruction …
… and one pending instruction …
… while the host sets up the next instruction by accessing Hydra’s registers
Instructions advance automatically through the instruction buffer’s stages
  Entering as they are posted to the OPCODE register
  Leaving as they complete their execution in Hydra’s vector pipeline

## Slide 86: Example: Square root using Newton’s method
Let’s look at a real-world example: Square roots
  Hydra does not have an all-in-one “square root” operation
  Instead, it provides an instruction that estimates 1/sqrt(x) to just a few bits of precision
Three iterations of Newton’s method then refine this estimate to full single precision
  If xk is an estimate of 1/sqrt(y) with relative error ek …
  Then a better estimate is xk+1 = (1/2) * (3*xk − y * xk3)
  It converges quadratically: ek+1 ≈ ek2 (see Hydra User’s Guide section 4.3.7 for details)
  hydra_vrsqrte() estimates x0 with |e0| < 2−3    x3 is accurate with |e3| < (((2−3)2)2)2 = 2−24
  Each Newton iteration becomes a hydra_vmulh() “multiply and halve”, a hydra_vmsub() “multiply and subtract”, and a hydra_vmul() “multiply”
  One final hydra_vmul() gives sqrt(y) = y * (1/sqrt(y))
hydra_vrsqrte(hydra_set_vl(N),
hydra_vector(results, HYDRA_FLOAT), // Output vector.
hydra_vector(data, HYDRA_FLOAT)); // Input vector.

## Slide 87: Example: Square root using Newton’s method
float inputs[N], results[N], temp[N];
hydra_vrsqrte(hydra_set_vl(N),
hydra_vector(results, HYDRA_FLOAT),
hydra_vector(inputs, HYDRA_FLOAT));
for (int iter = 0; iter < 3; iter++) {
// Iterate: results = results * (1.5 − (inputs * (results2) * 0.5)).
hydra_vmulh(0, // temp = inputs * results * 0.5.
hydra_vector(temp, HYDRA_FLOAT),
hydra_vector(inputs, HYDRA_FLOAT),
hydra_vector(results, HYDRA_FLOAT));
hydra_vmsub(0, // temp = 1.5 − (temp * results).
hydra_vector(temp, HYDRA_FLOAT),
hydra_scalar_float(1.5),
_,
hydra_vector(results, HYDRA_FLOAT));
hydra_vmul(0, // results *= temp.
hydra_vector(results, HYDRA_FLOAT),
_,
hydra_vector(temp, HYDRA_FLOAT));
}
hydra_vmul_w(0, // Now sqrt(inputs) = inputs * (1/sqrt(inputs)).
hydra_vector(results, HYDRA_FLOAT),
_,
hydra_vector(inputs, HYDRA_FLOAT));
Each N-element vector operation takes N cycles
  At 400 MHz (in Byrd)
  Plus a few cycles of instruction startup overhead to fill/empty Hydra’s data pipeline
  This startup overhead becomes negligible as N grows large
Total time for this algorithm is 11*N cycles (plus startup overhead)
  Division using Newton’s method takes 6*N cycles
Notes: For comparison: The SiFive E76 high-performance RISC-V CPU takes 33*N cycles for N fsqrt.s or fdiv.s instructions.

## Slide 88: Example: Square root with vector registers
Recall that macros like hydra_vector() set up a “vector register” inside Hydra
  These macros normally choose the next available vector register (among V0–V7) automatically
  An alternative form, hydra_set_vector(), lets you choose the vector register yourself
We can reduce overhead by putting our working vectors directly in chosen Vn registers:
float inputs[N], results[N], temp[N];
hydra_set_vl(N);
hydra_set_vector(HYDRA_V0, inputs, HYDRA_FLOAT);
hydra_set_vector(HYDRA_V1, results, HYDRA_FLOAT);
hydra_set_vector(HYDRA_V2, temp, HYDRA_FLOAT);
hydra_vrsqrte(0, HYDRA_V1, HYDRA_V0);
for (int iter = 0; iter < 3; iter++) {
hydra_vmulh(0, HYDRA_V2, HYDRA_V0, HYDRA_V1);
hydra_vmsub(0, HYDRA_V2, hydra_scalar_float(1.5), _, HYDRA_V1);
hydra_vmul(0, HYDRA_V1, _, HYDRA_V2);
}
hydra_vmul_w(0, HYDRA_V1, _, HYDRA_V0);

## Slide 89: Example: Square root with the SPU
Hydra’s Stored Program Unit can run a complete algorithm on its own inside Hydra
  Guided by a stored program made of vector operations and other MCU-like instructions:
  To run the program:
uint32_t sqrt_prog[100]; // An SPU program is just an array in RAM.
hydra_spu_begin(sqrt_prog, 100) { // Record the following sequence of Hydra operations in sqrt_prog[]:
hydra_vrsqrte(0, HYDRA_V1, HYDRA_V0); // In this context, each Hydra instr is recorded instead of running immediately.
for (int iter = 0; iter < 3; iter++) {
hydra_vmulh(0, HYDRA_V2, HYDRA_V0, HYDRA_V1);
hydra_vmsub(0, HYDRA_V2, hydra_scalar_float(1.5), _, HYDRA_V1);
hydra_vmul(0, HYDRA_V1, _, HYDRA_V2);
}
hydra_vmul(0, HYDRA_V1, _, HYDRA_V0);
hydra_spu_end();
}
float inputs[N], results[N], temp[N];
hydra_set_vl(N);
hydra_set_vector(HYDRA_V0, inputs, HYDRA_FLOAT);
hydra_set_vector(HYDRA_V1, results, HYDRA_FLOAT);
hydra_set_vector(HYDRA_V2, temp, HYDRA_FLOAT);
hydra_vstart_w(hydra_set_vpc(sqrt_prog));
Notice that the source code between the hydra_spu_begin() and the hydra_spu_end() is exactly the same as the non-SPU version of the code!

## Slide 90: Example: Floating-point FFT
Hydra 3 performed Fast Fourier Transforms as a single, all-in-one operation
  Very convenient, but the hardware was so expensive that we had to omit it in many chips!
  Also, inefficient because the full hardware FFT didn’t fit well with Hydra’s pipeline
Hydra 4 instead provides “building blocks” that allow an efficient pipelined FFT to be built as a firmware routine or SPU program that operates Hydra
  The algorithm, as expressed in complex numbers in the Hydra 4 User’s Guide:

## Slide 91: Example: Floating-point FFT (2)
The first step uses bit-reversed addressing to rearrange the inputs
  It also applies the arithmetic for M = 2 as a special case
float real[N], imag[N], temp[N], cosines[N/4];
int t = HYDRA_FLOAT;
#define REALE hydra_strided(real, t, 2)
#define REALO hydra_strided(real+1, t, 2)
#define IMAGE hydra_strided(imag, t, 2)
#define IMAGO hydra_strided(imag+1, t, 2)
#define TEMPE hydra_strided(temp, t, 2)
#define TEMPO hydra_strided(temp+1, t, 2)
hydra_set_vl(N);
hydra_vmov(0, hydra_vector(temp, t), hydra_bitrev(real, t, HYDRA_BITREV_STRIDE(N/2)));
hydra_set_vl(N/2);
hydra_vadd(0, REALE, TEMPE, TEMPO);
hydra_vsub(0, REALO, TEMPE, TEMPO);
hydra_set_vl(N);
hydra_vmov(0, hydra_vector(temp, t), hydra_bitrev(imag, t, HYDRA_BITREV_STRIDE(N/2)));
hydra_set_vl(N/2);
hydra_vadd(0, IMAGE, TEMPE, TEMPO);
hydra_vsub(0, IMAGO, TEMPE, TEMPO);

## Slide 92: Example: Floating-point FFT (3)
Then several steps use a “butterfly” mode to combine both inner loops of the FFT into one loop across N/2 elements
  And “cosine table” and “sine table” modes to expand a one-quadrant RAM table of cosines into full sin(x) and cos(x) functions
  Total execution time is about 4*N*log2(N) cycles (not counting instr startup overhead)
for (int M = 4; M <= N; M *= 2) {
uint32_t bfly_args = HYDRA_BFLY_M(M);
uint32_t sincos_args = HYDRA_SINCOS_NM(MAX_N, M) + HYDRA_SINCOS_HALF;
hydra_set_vl(N/2);
hydra_vmul(0, TEMPE, hydra_bfly(real+(M/2), t, bfly_args), hydra_cosine(cosines, t, sincos_args));
hydra_vmul(0, TEMPO, hydra_bfly(imag+(M/2), t, bfly_args), hydra_cosine(cosines, t, sincos_args));
hydra_vmadd(0, TEMPE, _, hydra_bfly(imag+(M/2), t, bfly_args), hydra_sine(cosines, t, sincos_args));
hydra_vmsub(0, TEMPO, _, hydra_bfly(real+(M/2), t, bfly_args), hydra_sine(cosines, t, sincos_args));
hydra_vsub(0, hydra_bfly(real+(M/2), t, bfly_args), hydra_bfly(real, t, bfly_args), TEMPE);
hydra_vsub(0, hydra_bfly(imag+(M/2), t, bfly_args), hydra_bfly(imag, t, bfly_args), TEMPO);
hydra_vadd(0, hydra_bfly(real, t, bfly_args), _, TEMPE);
hydra_vadd(0, hydra_bfly(imag, t, bfly_args), _, TEMPO);
}

## Slide 93: Example: Floating-point FFT (4)
Hydra has a “complex number addressing mode” to facilitate operations on complex numbers
  It optionally negates and/or swaps alternating vector elements, causing a single VADD or VMADD to perform 90° complex rotations, etc.
This, plus a few more refinements, gives a concise FFT algorithm that uses just 4*log2(N) Hydra operations each of length N
  See hydra4_test_fft2.c in the Hydra 4 test suite for other variants such as an SPU-based version
void hydra_fft(int N, cplx_float_t *data)
{
hydra_set_vl(N);
extern float cosines[MAX_N/4]; // First-quadrant table of cosines.
float temp[N]; // or temp[MAX_N] if variable length arrays cannot be used.
int t = HYDRA_FLOAT;
int temp_vec = hydra_set_vector(HYDRA_V7, temp, t);
uint32_t bitrev_args = HYDRA_BITREV_STRIDE(N);
hydra_vmov(0, temp_vec, hydra_bitrev(&data[0].re, t, bitrev_args));
hydra_vadd(0, hydra_strided(&data[0].re, t, 2),
hydra_complex(temp, t, HYDRA_COMPLEX_NODD),
hydra_complex(temp, t, HYDRA_COMPLEX_SWAP));
hydra_vmov(0, temp_vec, hydra_bitrev(&data[0].im, t, bitrev_args));
hydra_vadd(0, hydra_strided(&data[0].im, t, 2),
hydra_complex(temp, t, HYDRA_COMPLEX_NODD),
hydra_complex(temp, t, HYDRA_COMPLEX_SWAP));
for (int M = 4; M <= N; M *= 2) {
uint32_t bfly_args = HYDRA_BFLY_M(M*2);
uint32_t sincos_args = HYDRA_SINCOS_NM(MAX_N, M) +
HYDRA_SINCOS_HALF + HYDRA_SINCOS_DIV;
hydra_vmul(0, temp_vec, hydra_bfly(&data[M/2].re, t, bfly_args),
hydra_cosine(cosines, t, sincos_args));
hydra_vmadd(0, hydra_complex(temp, t, HYDRA_COMPLEX_SWAP), _, hydra_bfly(&data[M/2].re, t, bfly_args),
hydra_sine(cosines, t, sincos_args));
hydra_vsub(0, hydra_bfly(&data[M/2].re, t, bfly_args),
hydra_bfly(&data[0].re, t, bfly_args), temp_vec);
hydra_vadd(0, hydra_bfly(&data[0].re, t, bfly_args), _, temp_vec);
}
hydra_wait();
}

## Slide 94: Hydra 4
Architecture overview
  Introduction
  Using Hydra
    Examples
    Hydra registers
    Vector instructions
    Data types
    Addressing modes
    Stored program unit
    Documentation and tools
    Hydra 4.2 functionality
    Performance
  Hardware and implementation

## Slide 95: Hydra 4’s registers
Hydra has 14 host-accessible control registers
Also 16 host-accessible VnCFG / VnADDR registers that define eight vectors V0 … V7
All these registers are architecturally 32 bits wide
  (But some registers implement fewer bits)
  When Chimera is the host CPU, it can do 16-bit MOVs or 32-bit LMOVs to/from these registers
  Non-Chimera host CPUs, which use the AHB or APB bus or the Direct host interface to access Hydra, can do 8-, 16-, or 32‑bit reads or writes (usually 32 bits)
HYDRA_P->VL = 100;
HYDRA_P->V0CFG = 0x00000020;
HYDRA_P->V0ADDR = (int) results;
HYDRA_P->V1CFG = 0x00000010;
HYDRA_P->V1ADDR = (int) data;
HYDRA_P->V2CFG = 0x00005220;
HYDRA_P->V2ADDR = (int) inputs;
while (!(HYDRA_P->IRQ & 2)) { }
HYDRA_P->OPCODE = 0x00006210;

## Slide 96: Address registers
Hydra works in terms of physical RAM addresses with byte granularity
  These are ordinary pointers for RISC-V / ARM hosts, or “long pointers” for Chimera 4.2 hosts
hydra4_config.vh defines each chip’s RAM address width, `HYDRA_WIDTH_W = “W”
  Hydra 4 can be built with any W from 17 to 32
  Example: W = 17 for Chimera’s basic 64KW RAM space or Byrd A0’s 128KB DTIM RAM
  Example: W = 18 on Byrd B0, allowing Hydra to address 128KB DTIM + 56KB SYS_MEM RAM
  Example: W = 32 if Hydra wants to see the chip’s full AHB address space
Registers that hold addresses are W bits wide
  They ignore the data written to their high (32 − W) bits
  For example, if W = 20 and host firmware has a pointer into data RAM “0x60012345” …
  … the host can write 0x60012345 directly to V0ADDR, which will receive the RAM-relative 20-bit-wide address 0x12345
In Chimera systems, a compatibility feature also allows the host to use traditional Chimera 16-bit word-granular pointers (not applicable to SmartBridge or Byrd)

## Slide 97: Hydra 4 registers (shown for W = 20)
Name | Offset | Bit 31 | 23 |  | 15 |  | 7 | 0
OPCODE | +0x00 | Write an opcode here to post a vector instruction |  |  |  |  |  | 
VL | +0x04 | 0x000 |  | Vector length |  |  |  | 
VMA | +0x08 | 0x000 |  | Vector mask address |  |  |  | 
VPC | +0x0C | 0x000 |  | SPU program counter |  |  |  | 
G0 | +0x10 | General register G0 |  |  |  |  |  | 
G1 | +0x14 | General register G1 |  |  |  |  |  | 
IRQ | +0x20 | 0x00 | Error reason |  | Int ack |  | Int flags | 
IEN | +0x24 | 0x000000 |  |  |  |  | Int enable | 
MODES | +0x28 | PRIV_ONLY | DIS/EN |  | 0x00 |  | Rounding | 
PCOUNT | +0x2C | Performance counter |  |  |  |  |  | Event
STATUS | +0x30 | 0x0000 |  |  | Inverted flags |  | Status flags | 
COMPAT_OPCODE | +0x34 | 0x0000 |  |  | Write Hydra 3 opcode |  |  | 
VMCNT | +0x38 | 0x000 |  | Vector mask count |  |  |  | 
PROPS | +0x3C | Version 4.2.1 = “0x0421” |  |  | Properties |  |  | 
VnCFG | +0x40 + 8n | ARG |  |  |  | MODE | TYPE | 
VnADDR | +0x44 + 8n | 0x000 |  | Vector base address |  |  |  | 
8x

## Slide 98: Using Hydra in multiple threads, tasks, or cores
Most Synaptics firmware is written in terms of multiple “tasks”
  These could be Chimera threads, RTOS tasks, handlers, modules, or CPU cores all running at once
  What if several of these tasks want to use Hydra at the same time?
  One answer is to arbitrate access in the RTOS: In Hydra 3, this was the only answer
Hydra 4 supports multiple register contexts
  Multiple views of the register set just shown
  Eventually, there will be an option for multiple “full” register sets: Expensive!
  Full contexts would allow very fluid multi-tasked use of Hydra, but they are not yet implemented in Hydra 4.0–4.2 for Byrd and SmartBridge
By default (and implemented now), each additional register context is partial
  Most registers are shared, but each context has its own OPCODE, IRQ.BOUNCE, and IRQ.DONE
  This is enough to allow tasks to safely share Hydra on the granularity of SPU routines
  Alternatively, in Chimera systems, Hydra can integrate with Chimera’s hardware mutexes

## Slide 99: Hydra 4
Architecture overview
  Introduction
  Using Hydra
    Examples
    Hydra registers
    Vector instructions
    Data types
    Addressing modes
    Stored program unit
    Documentation and tools
    Hydra 4.2 functionality
    Performance
  Hardware and implementation

## Slide 100: Vector operations
Hydra 4 has a large repertoire of vector operations
  The hardware sees them as vector instructions for a vector processor
  To the C programmer, each vector operation looks like a function call
Almost all Hydra 4 operations take N “hclk” cycles plus a few cycles of startup overhead
  Where “N” is the vector length “VL”
  For matrices, N is the total number of matrix elements (N = VL = R*C)
  Convolutions and matrix multiplications take N*M cycles (startup overhead is paid just once)
  SIMD operation, when applicable, can reduce the number of cycles to ½ or ¼ normal (see later)
  “hclk cycles” = At the full HSO speed, e.g., ~400 MHz on Byrd, ~350 MHz on SB7900
  (On Chimera-based chips, Hydra 4, like Hydra 3, will run at twice Chimera’s pclk rate)
hydra_vrsqrte(hydra_set_vl(N), // Instruction modifier(s).
hydra_vector(results, HYDRA_FLOAT), // Output vector.
hydra_vector(data, HYDRA_FLOAT)); // Input vector.

## Slide 101: Vector operations: Basic arithmetic
Operation | … performs
hydra_vadd(m, dest, src1, src2) | dest[i] ← src1[i] + src2[i]
hydra_vsub(m, dest, src1, src2) | dest[i] ← src1[i] − src2[i]
hydra_vsubn(m, dest, src1, src2) | dest[i] ← − src1[i] − src2[i]
hydra_vmul(m, dest, src1, src2) | dest[i] ← src1[i] * src2[i]
hydra_vmuln(m, dest, src1, src2) | dest[i] ← − src1[i] * src2[i]
hydra_vneg(m, dest, src) | dest[i] ← − src[i]
“m” = instruction setup or modifier bits (0 if no setup/modifiers needed)
The operands dest, src1, src2, and src3 may have any combination of data types and addressing modes

## Slide 102: Vector operations: Fused multiply-add
Operation | … performs
hydra_vmadd(m, dest, src1, src2, src3) | dest[i] ← src1[i] + (src2[i] * src3[i])
hydra_vmsub(m, dest, src1, src2, src3) | dest[i] ← src1[i] − (src2[i] * src3[i])
hydra_vmsubr(m, dest, src1, src2, src3) | dest[i] ← − src1[i] + (src2[i] * src3[i])
hydra_vmsubn(m, dest, src1, src2, src3) | dest[i] ← − src1[i] − (src2[i] * src3[i])
These do the full computation, a + b*c, without rounding the intermediate product
  The “fused multiply-add” operation has many useful properties: See the Hydra 4 User’s Guide
Hydra’s VMADD is just as fast as a VMUL or a VADD alone
  The Multiply and the Add happen simultaneously, in different stages of Hydra’s pipeline
In the C language, the standard function fmaf(b, c, a) does a fused multiply-add

## Slide 103: Vector operations: Multiply-accumulate
Operation | … performs
hydra_vsum(m, dest, src) | dest ← ∑i src[i]
hydra_vmac(m, dest, src1, src2) | dest ← ∑i (src1[i] * src2[i]) “Fast mult-accum”
hydra_vdmac(m, dest, src1, src2) | dest ← ∑i (src1[i] * src2[i]) “Deterministic”
hydra_vomac(m, dest, src1, src2) | dest ← ∑i (src1[i] * src2[i]) “Fully ordered”
hydra_vcmac(m, dest, src1, src2) | dest[i] ← ∑j≤i (src1[j] * src2[j]) “Cumulative”
hydra_vconvo(m, dest, src1, src2) | Use VMAC as the kernel in a convolution
hydra_vmm(m, dest, src1, src2) | Use VMAC as the kernel in a matrix-multiply
Hydra offers several flavors of this operation
  VMAC, VOMAC, and VDMAC give three different useful trade-offs of speed and precision vs. ease of matching the result (with bit-for-bit the same rounding) in non-Hydra firmware code
  See the detailed description of Hydra’s ALU later in this presentation

## Slide 104: Vector operations: Division and square root
Operation | … performs
hydra_vrcpe(m, dest, src) | dest[i] ← 1 / src[i] “Estimate accurate to 6 bits”
hydra_vrcpe2(m, dest, src1, src2) | dest[i] ← 1 / src1[i] with special treatment of extreme values for src2[i] / src1[i]
hydra_vrsqrte(m, dest, src) | dest[i] ← 1 / sqrt(src[i]) “Estimate to 3 bits”
hydra_vrsqrte2(m, dest, src) | dest[i] ← 1 / sqrt(src[i]) with special treatment of extreme values for sqrt(src[i])
hydra_vdiv(m, dest, src1, src2) | dest[i] ← src1[i] / src2[i] (Red = not yet impl’d)
VDIV is not implemented in Hydra 4.0–4.2, but simple routines based on VRCPE can do:
  Accurate floating-point division in 6 cycles per quotient (much faster than VDIV would be!)
  IEEE compliant exactly rounded floating-point division in 10 cycles per quotient
  Exact integer division in 11 cycles per quotient (or 7 cycles for short integers)

## Slide 105: Vector operations: Other arithmetic
Operation | … performs
hydra_vadd3(m, dest, src1, src2, src3) | dest[i] ← src1[i] + src2[i] + src3[i] (integers)
hydra_vavg(m, dest, src1, src2) | dest[i] ← (src1[i] + src2[i]) / 2
hydra_vsubh(m, dest, src1, src2) | dest[i] ← (src1[i] − src2[i]) / 2
hydra_vmulh(m, dest, src1, src2) | dest[i] ← (src1[i] * src2[i]) / 2
hydra_vabs(m, dest, src) | dest[i] ← abs(src[i])
hydra_vasub(m, dest, src1, src2) | dest[i] ← abs(src1[i] − src2[i])
hydra_vcsign(m, dest, src1, src2) | dest[i] ← abs(src1[i]) * (src2[i] < 0 ? −1 : 1)
hydra_vshl(m, dest, src1, src2) | dest[i] ← src1[i] * (2src2[i]) (integer src2)
hydra_vshr(m, dest, src1, src2) | dest[i] ← src1[i] * (2−src2[i]) (integer src2)
hydra_vlog2(m, dest, src1, src2) | dest[i] ← floor(log2(src1[i])) + src2[i]

## Slide 106: Vector operations: Other arithmetic
Operation | … performs
hydra_vadd3(m, dest, src1, src2, src3) | dest[i] ← src1[i] + src2[i] + src3[i] (integers)
hydra_vavg(m, dest, src1, src2) | dest[i] ← (src1[i] + src2[i]) / 2
hydra_vsubh(m, dest, src1, src2) | dest[i] ← (src1[i] − src2[i]) / 2
hydra_vmulh(m, dest, src1, src2) | dest[i] ← (src1[i] * src2[i]) / 2
hydra_vabs(m, dest, src) | dest[i] ← abs(src[i])
hydra_vasub(m, dest, src1, src2) | dest[i] ← abs(src1[i] − src2[i])
hydra_vcsign(m, dest, src1, src2) | dest[i] ← abs(src1[i]) * (src2[i] < 0 ? −1 : 1)
hydra_vshl(m, dest, src1, src2) | dest[i] ← src1[i] * (2src2[i]) (integer src2)
hydra_vshr(m, dest, src1, src2) | dest[i] ← src1[i] * (2−src2[i]) (integer src2)
hydra_vlog2(m, dest, src1, src2) | dest[i] ← floor(log2(src1[i])) + src2[i]
When operating on integers, VSHL and VSHR are bitwise shifts, and VLOG2 finds the leftmost ‘1’ bit
When operating on floats, VSHL and VSHR scale the exponent and VLOG2 extracts the exponent

## Slide 107: Vector operations: Data motion
Operation | … performs
hydra_vmov(m, dest, src) | dest[i] ← src[i]
hydra_vmovn(m, dest, src) | dest[i] ← src[i] “Move with no side effects”
hydra_vmovlr(m, dest, src) | dest[i] ← src[i] “Move in left-to-right order”
hydra_vmov2(m, dest1, dest2, src1, src2) | dest1[i] ← src1[i] and dest2[i] ← src2[i]
hydra_vmov4(m, dest1, dest2, dest3, dest4) | dest1[i], dest2[i], dest3[i], dest4[i] ← G0
hydra_vxch(m, dest1, dest2) | dest1[i] ← dest2[i] and dest2[i] ← dest1[i]
hydra_vsel(m, dest, src1, src2) | dest[i] ← mask[i] ? src2[i] : src1[i]
hydra_vselq(m, dest, src1, src2, src3) | dest[i] ← Sine/Cosine argument reduction

## Slide 108: Vector operations: Gather/compact
Operation | … performs
hydra_vmovg(m, dest, k, src1, src2) | dest[i] ← src1[src2[i]*k] “Gather under index”
hydra_vmovs(m, dest, k, src1, src2) | dest[src2[i]*k] ← src1[i] “Scatter under index”
hydra_vmovc(m, dest, src, limit) | dest[j++] ← src[i] “Compact under mask”
hydra_vmovc2(m, dest1, dest2, src, limit) | dest1[j++] ← src[i] else dest2[k++] ← src[i]
hydra_vmovx(m, dest, src) | dest[i] ← src[j++] “Expand under mask”
hydra_vmovx2(m, dest, src1, src2) | dest[i] ← src1[j++] else dest[i] ← src2[k++]

## Slide 109: Vector operations: Bitwise operations
Operation | … performs
hydra_vand(m, dest, src1, src2) | dest[i] ← src1[i] & src2[i]
hydra_vandn(m, dest, src1, src2) | dest[i] ← src1[i] & ~src2[i]
hydra_vnand(m, dest, src1, src2) | dest[i] ← ~(src1[i] & src2[i])
hydra_vor(m, dest, src1, src2) | dest[i] ← src1[i] ¦ src2[i]
hydra_vorn(m, dest, src1, src2) | dest[i] ← src1[i] ¦ ~src2[i]
hydra_vnor(m, dest, src1, src2) | dest[i] ← ~(src1[i] ¦ src2[i])
hydra_vxor(m, dest, src1, src2) | dest[i] ← src1[i] ^ src2[i]
hydra_vxnor(m, dest, src1, src2) | dest[i] ← ~(src1[i] ^ src2[i])
hydra_vnot(m, dest, src) | dest[i] ← ~src[i]

## Slide 110: Vector operations: More bitwise operations
Operation | … performs
hydra_vbool(m, dest, src1, src2, src3) | dest[i] ← fG0(src1[i], src2[i], src3[i], mask[i]) bitwise
hydra_vandv(m, dest, src) | dest ← &i (src[i]) “Bitwise AND across N words”
hydra_vorv(m, dest, src) | dest ← ¦i (src[i])
hydra_vxorv(m, dest, src) | dest ← ^i (src[i])
hydra_vbrev(m, dest, src1, src2) | dest[i] ← bit reverse/rearrangesrc2[i] (src1[i])
hydra_vpop(m, dest, src) | dest ← ∑i popcount(src[i]) “Count ‘1’ bits”
hydra_vham(m, dest, src1, src2) | dest ← ∑i popcount(src1[i] ^ src2[i])
hydra_vclass(m, dest, src1, src2) | dest[i] ← classify_number(src1[i]) & src2[i]

## Slide 111: Vector operations: Comparison
Operation | … performs
hydra_vcmp_cond(m, dest, src1, src2) | dest[i] ← src1[i]  src2[i] ? 1 : 0
hydra_vcmpm_cond(m, mask, src1, src2) | mask[i] ← src1[i]  src2[i] ? 1 : 0
hydra_vcmpsel_cond(m, dest, src1, src2) | dest[i] ← src1[i]  G0 ? G1 : src2[i]
hydra_vnext_cond(m, dest, src1, src2) | dest ← first i for which src1[i]  src2[i]
hydra_vfind_cond(m, dest, src1, src2) | dest[j++] ← i if src1[i]  src2[i]
hydra_vfindt_cond(m, dest, src1, src2) | dest[j++] ← i if src1[i]  src2[i] and !(src1[i−1]  src2[i−1])
Hydra_vcount_cond(m, dest, src1, src2) | dest ← count of matches src1[i]  src2[i]
“cond” may be: eq, ne, lt, le, gt, ge (Basic numeric comparisons) ltlt, ltle, lelt, lele, nltlt, nltle, nlelt, nlele (0 < src1[i] < src2[i], etc.) aeq, ane, alt, ale, agt, age, a[n]ltlt, a[n]ltle (Compare by absolute value) class, nclass, ord, unord (Number classification)

## Slide 112: Vector operations: Min and Max
Operation | … performs
hydra_vmin(m, dest, src1, src2) | dest[i] ← min(src1[i], src2[i])
hydra_vamin(m, dest, src1, src2) | dest[i] ← min(src1[i], src2[i]) “Abs compare”
hydra_v[a]max(m, dest, src1, src2) | dest[i] ← max(src1[i], src2[i])
hydra_vminmax(m, dest1, dest2, src1, src2) | dest1[i] ← min(src1[i], src2[i]) and dest2[i] ← max(src1[i], src2[i]) “Sort a pair”
hydra_v[a]minv(m, dest, src) | dest ← mini (src[i]) “Min value across vector”
hydra_v[a]maxv(m, dest, src) | dest ← maxi (src[i])
hydra_v[a]mini(m, dest, src) | dest ← arg mini (src[i]) “Index of min”
hydra_v[a]maxi(m, dest, src) | dest ← arg maxi (src[i])

## Slide 113: Vector operations: Sorting and median filters
Operation | … performs
hydra_vmsort(m, dest, src1, src2) | dest[i] ← smaller of src1[j++], src2[k++]
hydra_vpsort(m, dest1, dest2) | swap as needed to establish dest1[i] ≤ dest2[i]
hydra_vmed(m, dest, src, src_k) | dest ← mediani(src[i], k) “k’th order statistic”
hydra_vmedr(m, dest, src, src_k) | dest ← mediani(src[i], N−k)
hydra_vcbin(m, dest, src1, src2) | dest[i] ← classify_in_bins(src1[], src2[i])
VMSORT (in Hydra 4.2 and later) implements a Merge Sort in about N * log2(N) cycles
  Also, VCMP + VMOVC2 implement the partitioning step of a Quicksort or Quickselect
VMED is not yet implemented in Hydra 4.0–4.2 for Byrd and SmartBridge
  Hydra’s VPSORT and VMSORT instructions are enough to construct a median filter that is much faster than any firmware implementation (17–24 cycles per output element, for a 3×3 filter)
  … though not as fast as VMED will be (9 cycles per output element)
Notes: Note, that’s not O(N log2(N)), it’s actually 1 * N * log2(N) cycles!

## Slide 114: Vector operations: Cryptographic
Operation | … performs
hydra_vcrc(m, dest, src1, src2) | dest ← CRCi(src1[i]) “Cyclic redundancy check”
hydra_vrand(m, dest, src1, src2) | dest[i] ← CRCj≤i(src1[j]) “Random numbers”
hydra_vxmadd(m, dest, src1, src2, src3) | “Extended-precision integer multiply-add”
hydra_vclmul(m, dest, src1, src2) | “Extended-precision carry-less multiplication”
hydra_vaes(m, dest, src1, src2) | “AES-128/-192/-256 encryption / decryption”
hydra_vxxtea(m, dest, src1, src2) | “XXTEA 128-bit encryption / decryption”
hydra_vsha2m(m, dest, src1, src2) | “SHA-256/-224 message schedule phase”
hydra_vsha2h(m, dest, src1, src2) | “SHA-256/-224 hash calculation phase”
  VCRC computes a CRC32 (or narrower) hash with any CRC polynomial
  VRAND uses the same CRC machinery, as a 32-bit LFSR, to generate pseudo-random numbers
  VXMADD accelerates the main calculation in public-key DSA/RSA cryptographic systems
  VAES, VCLMUL, and VSHA2M/H implement widely used NIST standards for encryption and hashing

## Slide 115: Other operations: Controlling Hydra
Operation | … performs
hydra_vstart(m) | Start the stored program unit (SPU) at the program address given by VPC
hydra_vcall(m, n) | Start SPU at subroutine #n in program library
hydra_vnop(m) | No operation
hydra_wait() | Wait for Hydra to be Idle (all instrs are done)
hydra_wready() | Wait for Hydra to be Ready (to post an instr)
HYDRA_RESET() | Reset Hydra to idle state

## Slide 116: Instruction timing
Most Hydra 4 instructions run at a speed of one iteration per hclk cycle
  If VL = N  (N + TSU) hclk cycles: N plus a few (“TSU”) cycles of instruction startup overhead
  Same for all data types, all addressing modes, etc.
A few instructions take more time for complex calculations:
  VOMAC: 4 * N hclks (for special uses only; normal VMAC runs at full speed)
  Convolutions and matrix multiplications: N * M cycles
  VDIV: TBD (not yet implemented in Hydra 4.0–4.2)
  VCRC: 2 hclks per input byte
  VRAND: 1–8 hclks per generated 32-bit result (depending on desired quality of randomness)
  VCLMUL: 8 hclks per 32-bit result
  VAES: 10.25 hclks per input byte (AES-128)
  VXXTEA: 9.75 hclks per input byte
  VSHA2: 4.875 hclks per input byte

## Slide 117: Instruction startup overhead
How many cycles of overhead “TSU” are there?
  It depends on factors including the instruction, addressing modes, and memory alignment, and on how Hydra is configured in a chip
  For a simple arithmetic instruction (e.g., VADD, VMUL, or VMADD) with simple linear vectors:
    In Hydra 4.0 on Byrd A and Smartbridge: TSU = 14 cycles
    In Hydra 4.2 on Byrd B and future chips: TSU = 9 or 10 cycles
  Therefore, TSU has a small effect if N is very large, but overhead can dominate as N gets small
   Hydra is meant to be used with reasonably large vectors, e.g., at least a dozen elements
  A future version of Hydra 4 will include “instruction joining” to help reduce the impact of TSU (see later)
Where does the overhead come from?
  Hydra has a deep pipeline
  This allows it to clock very fast, but it creates a long latency from input to output

## Slide 118: Vector processing pipeline
Hydra’s net throughput is one vector element per cycle, but each vector element passes through many stages of processing from input to output:
  Generate address and bank arbitration for src channel
  Send read request to RAM
  Receive read data from RAM
  Unpack data in ALU according to its type
  ALU multiplier first stage
  ALU multiplier second stage
  ALU adder
  ALU normalization
  ALU round, saturate, and format result
  Pack result for dest channel
  Bank arbitration for dest channel
  Send write request to RAM
  Write occurs in RAM
In the middle of a long vector operation, all 13 of these stages are busy during every cycle, with 13 successive vector elements “in flight”
Although this may seem like many stages, it is comparable to the E76 CPU’s 8-stage pipeline, accounting for the fact that Hydra can load, do arithmetic, and store all at once

## Slide 119: Vector operations: Instruction modifiers “m”
Operation | … performs
hydra_set_vl(n) | VL ← n
hydra_set_vma(mask) | VMA ← address_of(mask)
hydra_mask_if(mask) | VMA ← address_of(mask), enable masking
hydra_mask_else(mask) | VMA ← address_of(mask), enable complemented masking
hydra_mask_xm(mask) | VMA ← address_of(mask), enable “extra mask”
hydra_rz() | Force round-toward-zero mode for this instr
hydra_ru() | Force round-upward (“ceiling”) for this instr
hydra_rd() | Force round-downward (“floor”) for this instr
hydra_rn(), _rnu(), _rna(), _ra() | Force other rounding modes for this instr
hydra_convo(), hydra_mm() | Convolution or matrix-multiply mode applied to any scalar-producing instruction

## Slide 120: Opcode format
Every Hydra 4 instruction is defined by a 30-bit opcode
  Firmware writes this opcode to Hydra’s OPCODE register to start a vector operation
Hydra 4’s wide opcode allows a clean format with three or four operand fields and room for many instructions
All the operands dest, src1, src2, and src3/dest2 support the same choices: Any vector Vn, or any scalar in a Gn register
  “Scalar”  Same value for all “i”
Plus modifier bits that control vector masking, flags, rounding, and overlapped execution
Instruction
src2
src1
dest
Modifiers
src3/dest2/ cond
Instr

## Slide 121: Vector instructions
There is plenty of room still free in the space of 256 + 40 = 296 possible instruction opcodes
  We can make future improvements without cramming new instructions into odd corners of a cramped encoding (as happened in Hydra 3)

## Slide 122: Vector mask
Any instruction can generate a vector mask from any selected status flag
  Vector compare (VCMP) is just an instruction that generates 0-or-1 bits that reflect various comparisons
Any instruction can be conditional on the true or complemented mask
  Masking VCMP itself forms an AND or OR combination of conditions
The vector mask also serves as “carry” or “borrow” bits for arithmetic
  But because Hydra 4 can work directly with 32-bit integers, we will rarely need it
VM_EN and FLAG_EN are no longer “sticky” modes, as they were in Hydra 3

## Slide 123: Indexed addressing and sparse masks
Indexed addressing uses one vector as an index into another: vec1[ vec2[i] ]
  Hydra 3 allowed all three operands at once (dest, src1, src2) to use indexed addressing
  Seems cool… But it is very expensive in hardware, totally unlike any other vector architectures, and never used in real Synaptics firmware!
Hydra 4 replaces this with two specialized indexing instructions
  VMOVG (move and gather) and VMOVS (move and scatter)
  Just one indexing path in hardware that uses the src2 RAM channel for indexes: Much simpler!
Only one use was ever suggested for Hydra 3’s “indexed-everything” mode:
  Use indexing to operate on sparse data, e.g., selected by a rarely-true condition
  On Hydra 3, this would be more efficient than vector masks if the mask has only sparse ‘1’s
  Hydra 4’s solution: Handle sparse vector masks more efficiently
  This was the right solution all along! Sparse vector masks are one of those things that people requested for years… but I could never implement because Hydra 3’s logic was just too obscure
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
vm[i] | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0

## Slide 124: Other things done differently from Hydra 3
No all-in-one “VFFT” instruction for Fast Fourier Transforms
  Instead, Hydra 4 has a set of FFT addressing modes that allow firmware to implement the FFT algorithm efficiently (see the example earlier)
  This fits better into Hydra’s pipeline structure  Significantly faster than Hydra 3’s VFFT
    About 4 N log2(N) hclk cycles + O(log2(N)) overhead for a floating-point FFT
  Each mode can be calculated cheaply  FFTs are a standard capability, not a high-cost option
  Much more flexible  We can finally provide non-power-of-two strides in FFTs
Hydra 3’s VGEN instruction becomes “pattern mode” in Hydra 4
  The address pattern of any addressing mode can be used as a sequence of integers
  Basically, the addresses bypass the RAM and are used directly as data
  Different addressing modes can generate: Consecutive integers, arithmetic sequences, scalar constants, sawtooth waves, triangle waves, stairsteps, the bit-reversal function, and more
  Any instruction can use a pattern as any source operand
  Example: Tabulating a function using its power series

## Slide 125: Other things done differently (2)
Convolutions are generalized into a flexible “convolution mode”
  All accumulation-style instructions can work in convolution mode (both 1D and 2D)
  Convolving VMAC creates an FIR filter
  Convolving VMAC with packed data gives a fast + compact neural network!
  Convolving VMED creates a median filter
  Convolving VMAXV or VMINV creates a max or min filter or a neural net “maxpool” layer
  Convolving VHAM optimizes our “Hamming distance” fingerprint matching loop, etc…
Matrix multiplication also generalizes to work with any two-input accumulation
  Applied to VMAC, this gives a standard matrix multiply
  Applied to VHAM, it performs Hydra 3’s VMHAM operation
  Applied to VNEXT, it granularizes vector values using a table of thresholds
  Etc…

## Slide 126: Padded convolutions
Currently, Hydra 3 and 4.0–4.2 do not support automatic “padding” in convolutions
  For example, convolving a 5x5 kernel over a 14x19 image gives a 10x15 result with just the interior pixels where the kernel entirely overlaps the input image
  Often, we have a 10x15 input image that we want to filter into another 10x15 image …
  … where the border pixels are padded, e.g., with implicit zeroes or duplicate values
  Currently, users must implement such padding “by hand” in firmware
    Compute the edge pixels in a firmware loop, or using Hydra 1D ops, or create an explicitly padded image
  The Hydra 4 User’s Guide defines a feature to do padding in hardware, but it is not yet implemented in Hydra 4.0–4.2
    There just wasn’t time for Byrd / SmartBridge

## Slide 127: Hydra 4
Architecture overview
  Introduction
  Using Hydra
    Examples
    Hydra registers
    Vector instructions
    Data types
    Addressing modes
    Stored program unit
    Documentation and tools
    Hydra 4.2 functionality
    Performance
  Hardware and implementation

## Slide 128: Data types
Each source and destination vector has a data type
Most Hydra 4 instructions accept any mix of types in their inputs and result
Some things that were special instructions in Hydra 3 are now just cases of VMOV
  For example, VFFLOAT “convert integers to floats” and VFROUND “round floats to integers” now can be done simply as VMOV’s with different src and dest types
Many things that were modes in Hydra 3 (SIGNED, SHIFT, SATURATE, INT32) are now just part of the vector type
The only real “mode” now is MODES.ROUND, which firmware will hardly ever need to change

## Slide 129: Numbers
Hydra 4 supports a variety of data types:
  Fully IEEE-compatible single-precision floats
  Two flavors of 16-bit short floats
  Signed and unsigned 8-, 16-, and 32-bit integers and fixed-point numbers
  Packed K-bit integers, fixed, or “Posit” floats for any K from 1 to 32
← IEEE-standard half precision, as in RISC-V and ARM
← A popular format in the NN/AI/ML community

## Slide 130: Data types: Signed integers
Symbol | Data values
HYDRA_INT32 | 32-bit signed integers
HYDRA_INT16 | 16-bit signed integers
HYDRA_INT8 | 8-bit signed integers
HYDRA_INT | Signed integers of this machine’s “int” type
HYDRA_LONG | Signed integers of this machine’s “long” type
HYDRA_SHORT | Signed integers of this machine’s “short” type
HYDRA_CHAR | Signed integers of this machine’s “char” type
These are saturating types: An out-of-range result will saturate to the most positive or most negative representable number

## Slide 131: Data types: Unsigned integers
Symbol | Data values
HYDRA_UINT32 | 32-bit unsigned integers
HYDRA_UINT16 | 16-bit unsigned integers
HYDRA_UINT8 | 8-bit unsigned integers
HYDRA_UINT | Unsigned integers of machine’s “int” type
HYDRA_ULONG | Unsigned integers of machine’s “long” type
HYDRA_USHORT | Unsigned integers of machine’s “short” type
HYDRA_UCHAR | Unsigned integers of machine’s “char” type
These, too, are saturating types: An out-of-range result will saturate to the most positive representable number (or to 0 if negative)

## Slide 132: Data types: Truncating unsigned integers
Symbol | Data values
HYDRA_UTRUNC32 | 32-bit truncating unsigned integers
HYDRA_UTRUNC16 | 16-bit truncating unsigned integers
HYDRA_UTRUNC8 | 8-bit truncating unsigned integers
HYDRA_LWORD | Raw long-words of bits (same as UTRUNC32)
HYDRA_SWORD | Raw short-words of bits
HYDRA_BYTE | Raw bytes of bits
These truncating types take the low K bits of a result and discard any higher bits
  In other words: Overflows act the same as they do in C-language integer arithmetic
  In all of Hydra’s other types, out-of-range numbers instead saturate to fit in the K-bit range
  This distinction matters only in dest operands: In src operands, UTRUNC32 == UINT32, etc.

## Slide 133: Data types: Truncating signed integers
Symbol | Data values
HYDRA_TRUNC32 | 32-bit truncating signed integers
HYDRA_TRUNC16 | 16-bit truncating signed integers
HYDRA_TRUNC8 | 8-bit truncating signed integers
Hydra 4.0—4.1 did not include signed counterparts of the HYDRA_UTRUNCnn types
  The result is the same if you write to a signed or unsigned truncating dest
But there are some secondary benefits to including signed-TRUNC types in the system
  E.g., the setting of the Overflow status flag depends on the signed-ness
  And it is convenient to be able to use the same truncating-typed vector as both src and dest
  Therefore, Hydra 4.2 introduces “signed” versions of the truncating integer types
  When building for Hydra 4.0—4.1, “HYDRA_TRUNCnn” is treated as a synonym for “_UTRUNCnn”

## Slide 134: Data types: Fixed-point numbers
Symbol | Data values
HYDRA_FIX32(M) | 32-bit signed fixed-point with M = 0…32 fraction bits (and 32−M integer+sign bits)
HYDRA_FIX16(M) | 16-bit signed fixed-point with M = 0…16
HYDRA_FIX8(M) | 8-bit signed fixed-point with M = 0…8
HYDRA_UFIX32(M) | 32-bit unsigned fixed-point with M = 0…32
HYDRA_UFIX16(M) | 16-bit unsigned fixed-point with M = 0…16
HYDRA_UFIX8(M) | 8-bit unsigned fixed-point with M = 0…8
Fixed-point numbers are like saturating integers scaled by 2−M
  An algorithm can choose M based on the data’s known range and accuracy
  M effectively puts the “decimal point” at some position within the digits
  Known as “fixed point” (vs. floating point) because M is constant across all the vector elements

## Slide 135: Data types: Floating-point numbers
Symbol | Data values
HYDRA_FLOAT32 | 32-bit (fully IEEE-compatible single precision) floating-point numbers
HYDRA_FLOAT16 | 16-bit (IEEE half-precision) floats
HYDRA_BFLOAT16 | 16-bit “BFLOAT”-style floats
HYDRA_FLOAT | Synonym for HYDRA_FLOAT32
HYDRA_HFLOAT | Synonym for HYDRA_FLOAT16
HYDRA_BFLOAT | Synonym for HYDRA_BFLOAT16

## Slide 136: Data types: Posits
Hydra 4 also supports an alternative floating-point format called “Posits”
  https://posithub.org/docs/posit_standard-2.pdf
  https://posithub.org/docs/Posits4.pdf
  When used with Hydra’s packed addressing mode, Posits can pack floating-point numbers into any number (1–32) of bits with a good and flexible trade between precision and dynamic range
Symbol | Data values
HYDRA_POSIT32(M) | 32-bit Posits with M = 0…3 exponent bits
HYDRA_POSIT16(M) | 16-bit (or smaller) Posits
HYDRA_POSIT8(M) | 8-bit (or smaller) Posits
NaN

## Slide 137: SIMD operation
In computer architecture, SIMD (Single Instruction, Multiple Data parallelism) means splitting the normal data path (e.g., 32 bits wide for Hydra 4) into multiple lanes to process several small data items at once (e.g., 4 bytes or 2 short words per cycle)
Hydra 4.2.0 (non-”Junior”) includes a limited SIMD capability:
  VMAC / VSUM / VMM will operate on 8-bit integers at 4x speed under suitable conditions
  … i.e., when the vectors or matrix rows are a multiple of 4 bytes long, 4-byte-aligned in RAM, not vector-masked, etc.
With SIMD-mode VMM, Hydra 4.2 at 400 MHz (e.g., as found on the DIG2409B0 chip) can evaluate fully-connected neural networks at a speed of over 3 GOPS (3 billion add-or-multiply operations per second)
  This is more than 10x faster than firmware on a RISC-V E76 can achieve
  More than 20x faster than Chimera firmware
Future versions of Hydra will add SIMD treatment for other instructions and data types

## Slide 138: Hydra 4
Architecture overview
  Introduction
  Using Hydra
    Examples
    Hydra registers
    Vector instructions
    Data types
    Addressing modes
    Stored program unit
    Documentation and tools
    Hydra 4.2 functionality
    Performance
  Hardware and implementation

## Slide 139: Addressing modes
Each source or destination vector has an addressing mode
The addressing mode defines where each i’th vector element appears in RAM relative to the vector’s base address
Most Hydra 4 instructions accept any mix of modes in their inputs and result
Some things that were special instructions in Hydra 3 (e.g., VPACK, VMT) can be done as simply VMOV’s with different src and dest modes

## Slide 140: Addressing modes: Basic vectors and scalars
Notation | Addressed as
hydra_vector(base, type) | Linear vector in consecutive RAM locations
hydra_strided(base, type, stride) | Strided vector: base + i*stride
hydra_ostride(base, type, offset, stride) | Strided with offset: base + offset + i*stride
hydra_mscalar(base, type) | Scalar number replicated across the vector (the number comes from RAM)
hydra_scalar_int(x) | Scalar INT32 number x encoded directly (passed using Hydra’s G0 or G1 register) (The constants x = 0 and x = 1 can be encoded without using any Gn register)
hydra_scalar_float(x) | Scalar FLOAT32 number x encoded directly (passed using Hydra’s G0 or G1 register)
hydra_rscalar(reg, type) hydra_rscalar_int/float(reg, type, x) | Scalar number of any type stored in any Hydra register

## Slide 141: Addressing modes: Special modes
Notation | Addressed as
hydra_neg_vector(base, type) | A negated view of a linear source vector: The values are negated (as if by VNEG) as they come from RAM into Hydra’s arithmetic unit
hydra_abs_vector(base, type) | A linear source vector whose values are absolute-valued (as if by VABS) as they come
hydra_half_vector(base, type) | A multiplied-by-½ view of a vector in RAM
hydra_double_vector(base, type) | A multiplied-by-2 view of a vector in RAM
hydra_circular(base, type, mod) | Circular addressing: base + (i % mod)
hydra_offset_circ(base, type, mod, i0) | Offset-circular addressing: base + (i+i0) % mod
hydra_nested(base, type, args) | A double- or triple-nested repeating pattern of memory accesses, like a combination of circular and repeated-column modes

## Slide 142: Addressing modes: Matrix modes
Notation | Addressed as
hydra_matrix(base, type, C) | An RxC matrix of width C, height R = VL/C, row stride = C, and column stride = 1
hydra_tmatrix(base, type, R) | An RxC matrix which is the transposed view of a CxR matrix in the RAM whose width is R, C = VL/R, row stride = R, column stride = 1
hydra_gmatrix(base, type, C, rstride, cstride) | A matrix with general R, C, row stride, and column stride (the strides are passed in Hydra’s G0 or G1 register)
hydra_rrmatrix(base, type, C) | An RxC “repeated row” matrix where C = width, R = VL/C, row stride = 0, column stride = 1 (actually same as “circular addressing”)
hydra_rcmatrix(base, type, C) | An RxC “repeated column” matrix where C = width, R = VL/C, row stride = 1, column stride = 0

## Slide 143: Addressing modes: FFT-related modes
Notation | Addressed as
hydra_bfly(base, type, args) | FFT butterfly addressing
hydra_bitrev(base, type, args) | FFT bit-reversed addressing
hydra_cosine(base, type, args) | Cosine function from cosine table
hydra_sine(base, type, args) | Sine function from the same cosine table
hydra_complex(base, type, args) | Complex numbers rotated on the complex plane by a multiple of 90º and/or conjugated, where modes encodes any combination of swapping even-with-odd elements, negating even elements, negating odd elements, and/or absolute-valuing, halving, or doubling all elements
“args” is a bit mask of mode-related options such as HYDRA_BITREV_STRIDE(stride) or HYDRA_COMPLEX_SWAP + HYDRA_COMPLEX_ABS

## Slide 144: Addressing modes: Packed mode
Notation | Addressed as
hydra_packed(base, type, K_args) | K-bit signed or unsigned integers, fixed-point numbers, or Posit-style floats packed into long words, short words, or bytes, with initial bit offset k0 and with kgap bits between items
E=8, K=8, k0=0, kgap=0
E=8, K=8, k0=4, kgap=0
E=16, K=8, k0=4, kgap=0
E=16, K=8, k0=0, kgap=4
E=16, K=8, k0=4, kgap=4
E=16, K=4, k0=0, kgap=0
E=32, K=3, k0=6, kgap=3
E=32, K=1, k0=0, kgap=0

## Slide 145: Addressing modes: Other modes
Notation | Addressed as
hydra_mask_gen(mask) | In the dest operand position, generate a vector mask showing which results are non-zero (the results themselves are discarded)
hydra_mask_flag(mask) | Generate a vector mask recording a given status flag for each vector element
hydra_mask2_gen(base, type, mask, args) hydra_mask2_flag(base, type, mask, args) | Save the numeric results in a linear vector, and also generate a vector mask from a status flag
hydra_null_vector(type) hydra_null_scalar(type) | Null data source or sink of the indicated type; delivers 0’s as src; discards data as dest

## Slide 146: Addressing modes: Pattern mode
Notation | Generated as
hydra_pattern(a, b) | The integer arithmetic sequence a + (b*i)
hydra_rrpattern(a, mod) | The integer sequence a + (i % mod)
hydra_rcpattern(a, div) | The integer sequence a + floor(i / div)
hydra_gpattern(a, C, rstride, cstride) | An integer sequence based on the general matrix addressing pattern
hydra_patmode(mode, esize, base, args…) (encoded as any mode with type = PATTERN) | Integer sequence according to the mode
Hydra’s pattern mode generates a pattern of integers based on the sequence of addresses produced by any chosen addressing mode
  It bypasses the RAM and uses the address sequence itself as the source data
  It can generate: Arithmetic sequences, sawtooths, stairsteps, triangle waves, bit-reversal, …

## Slide 147: Hydra 4
Architecture overview
  Introduction
  Using Hydra
    Examples
    Hydra registers
    Vector instructions
    Data types
    Addressing modes
    Stored program unit
    Documentation and tools
    Hydra 4.0 functionality
    Performance
  Hardware and implementation

## Slide 148: Stored program unit
Hydra 3 introduced an SPU for autonomous operation with no firmware handholding
This especially helps non-Chimera CPUs with their clumsy interrupts, etc.
But Hydra 3’s SPU was so “strange” and intricate that people didn’t use it!
Hydra 4 has a redesigned SPU
A simple SPU program is just a list of Hydra vector instructions ending with a VSTOP (opcode 0x0)
Notes: This image was found on Google Images; attribution is now lost.

## Slide 149: Stored program unit
Hydra 3 introduced an SPU for autonomous operation with no firmware handholding
This especially helps non-Chimera CPUs with their clumsy interrupts, etc.
But Hydra 3’s SPU was so “strange” and intricate that people didn’t use it
Hydra 4 has a redesigned SPU
A simple SPU program is just a list of Hydra vector instructions ending with a VSTOP (opcode 0x0)
More complex SPU programs can do lots of things …

## Slide 150: Stored program unit (continued…)
The SPU can do more than simply issue a fixed sequence of vector opcodes
The SPU has its own instruction set for setting up vector operands and other register values
The SPU can operate on any Hydra registers while the rest of Hydra is busy with a vector operation (and the rest of the host CPU system may be busy doing unrelated work)

## Slide 151: Stored program unit (continued…)
More generally, SPU opcodes are instructions like those of a simple microcontroller
SPU programs can have their own conditional tests, loops, subroutines, variables, and so on
If the algorithm does not use all eight vector registers V0—V7, the spare VnCFG’s and VnADDR’s can serve as extra working registers for the SPU program

## Slide 152: Stored program unit (continued…)
But note that the SPU is not meant to be a fast microprocessor!
  The SPU uses a very simple sequencer that takes several cycles for most SPU instructions
  For example, the SPU has just one port for reading or writing Hydra registers, so VADDR3 takes at least three cycles to read registers “R” and “S” and to write to register “D”
  The SPU’s job is to be cheap and simple, while just fast enough to set up Hydra vector operations efficiently

## Slide 153: Hydra 4
Architecture overview
  Introduction
  Using Hydra
    Examples
    Hydra registers
    Vector instructions
    Data types
    Addressing modes
    Stored program unit
    Documentation and tools
    Hydra 4.2 functionality
    Performance
  Hardware and implementation

## Slide 154: Hydra 4 User’s Guide
The Hydra 4 User’s Guide describes how to use Hydra 4
  How to program it
  Detailed descriptions of every instruction, addressing mode, register, and feature
  Algorithms such as sqrt(), exp(), FFTs, merge sorts, median filters, neural nets, etc.
  How to integrate it into a chip’s hardware
A public version will be available soon on github.com/synaptics-hydra

## Slide 155: Hydra 4 tools
No special tools are required to program Hydra 4
  The hydra4_defs.h header file defines macros such as hydra_vadd_w() for invoking Hydra
  It is self-contained: No run-time library is needed; no special compiler or RTOS support
  It works with the host CPU’s standard C or C++ compiler and debugger
#include "hydra4_defs.h"
float scalarProduct(int len, float *veca, float *vecb)
{
float result;
HYDRA_INITIALIZE(); // Normally this is called just once at startup.
// Set result = sum(veca[i] * vecb[i] for i=0…len−1).
hydra_vmac_w(hydra_set_vl(len),
hydra_mscalar(&result, HYDRA_FLOAT),
hydra_vector(veca, HYDRA_FLOAT),
hydra_vector(vecb, HYDRA_FLOAT));
return result;
}
This function is complete; nothing else needed 

## Slide 156: A true Hydra “compiler”?
Wouldn’t it be great if we could simply write,
… and this would compile to a Hydra operation, if the target chip includes Hydra?
Vectorizing compilers do exist
  The Cray-1 had a vectorizing FORTRAN compiler
  OpenCL is a good modern example, or automatic vectorization of ordinary C loops
Could we port OpenCL to Hydra? Yes, if we had an army of compiler people …
  In other words, not for us, not right now anyway
  (Actually, for a RISC-V compiler it would not be that hard: Modern GCC can support vectorization)
float scalarProduct(int len, float *veca, float *vecb)
{
float sum = 0.0;
for (int i = 0; i < len; i++)
sum += (veca[i] * vecb[i]);
return sum;
}

## Slide 157: Porting legacy Hydra 3 firmware to Hydra 4
Synaptics touch and fingerprint firmware includes lots of code written for Hydra 3
  Most older code uses “HOCA_xxx” constants to painfully construct the Hydra 3 opcode
  Some newer code uses “Hydra assembler” macros to express the Hydra 3 opcode symbolically
Hydra 4’s compatibility mode makes it easy to port either style of Hydra 3 firmware to run on Hydra 4
Functions like these, originally written
for Hydra 3, can compile and run as-is in Hydra 4’s compatibility mode

## Slide 158: Compatibility mode
If you write a Hydra 3-style 16-bit opcode to Hydra 4’s COMPAT_OPCODE register …
  Hydra’s instruction decoder will [attempt to] translate it into a modern Hydra 4 operation
  … using a defined mapping from Hydra 3 registers onto Hydra 4’s register set
Simply use the hydra4_compat.h header file in place of Hydra 3’s hydra_base.h or hydra_registers_0x0310.h
  It defines the same Hydra 3 symbols, fields, types, and names as those old headers, all redefined appropriately for Hydra 4’s compatibility mode
  Most legacy source code that uses the Hydra 3 headers can build unchanged with hydra4_compat.h
  If desired, a single firmware source routine can build for either Hydra 3 or Hydra 4 depending on the target chip

## Slide 159: HydraSim simulator
HydraSim is a software simulator that models all versions of Hydra
  It now covers Hydra 4.0–4.2 as well as the older versions
  HydraSim gives bit-accurate answers for all Hydra instructions, plus timing estimates
  Developed by Adam Greenblatt (thanks, Adam!)
Chimera’s ChimSim simulator has HydraSim built-in
  ChimSim invokes it automatically when Chimera firmware uses Hydra
HydraSim is a library that can integrate into other simulators, as needed
  If we use a RISC-V instruction-level simulator to develop firmware for chips like Byrd …
  … we can modify that simulator to call HydraSim, just as ChimSim does
HydraSim can be integrated into any C/C++ program

## Slide 160: Hosted simulation with HydraSim
HydraSim also allows “hosted” development and testing of firmware that uses Hydra:
  Compile the firmware as a native x86 program under Windows or Linux
  Use –DHYDRA_HOSTED_SIM on the compilation command line
  Link with hydra4_hosted_hydrasim.c and hydrasim.a
Firmware algorithms can now be tested and debugged with all the tools and facilities of a large computer:
  Debug with GDB or Eclipse
  Use features that would be impractical in real firmware: double-precision floats, printf(), file I/O, huge data arrays, etc.
In hosted mode, every Hydra macro such as hydra_vadd_w(…), hydra_vector(…), etc., is automatically directed to the HydraSim simulator in lieu of using real Hydra hardware

## Slide 161: SIMT4 simulator
SIMT4 is a detailed simulator for Chimera chips
  It has a cycle-accurate simulation model of the Chimera CPU, and it models a chip’s peripherals, including Hydra, with the peripheral’s exact Verilog source code
  Its VSIMT4 graphical interface can debug integrated systems of firmware + hardware
  When firmware uses Hydra 4, the Hydra Viewer shows Hydra’s instruction buffer, arithmetic pipeline, and RAM channels and bank interfaces in detail

## Slide 162: HydraMath library
HydraMath is a relatively simple software library that exactly emulates the numeric results of most Hydra instructions
  … but not all the addressing modes, registers, and other Hydra features
  HydraMath also can convert numbers to or from any of Hydra’s supported data formats
  It is lightweight and easier to use than HydraSim in scripting environments, etc.
  HydraSim internally uses HydraMath to model Hydra’s arithmetic precisely

## Slide 163: Hydra 4
Architecture overview
  Introduction
  Using Hydra
    Examples
    Hydra registers
    Vector instructions
    Data types
    Addressing modes
    Stored program unit
    Documentation and tools
    Hydra 4.2 functionality
    Performance
  Hardware and implementation

## Slide 164: Implemented so far…
The full Hydra 4 User’s Guide describes lots of functionality
There wasn’t time to implement all of it for Byrd’s and SmartBridge’s Hydra 4.0
  But it certainly includes all functionality we currently use in our touch firmware with Hydra 3
  And it includes FFT support (needed for Byrd)
  And cryptographic support (may be needed for SmartBridge or Byrd)
In fact, most features in the Hydra 4 User’s Guide have been implemented

## Slide 165: Not yet implemented, omitted from Byrd
The following features from the full User’s Guide didn’t make it into SmartBridge / Byrd, but they can be added for future chips (especially if people ask for them):
  General division (VDIV)
  Fast median filters (VMED, VMEDR)
  Optimization of sparse vector masks
  Instruction “joining” optimization
  Faster “SIMD” treatment of 8- and 16-bit integer types (limited support appears in Hydra 4.2)
  Automatic edge “padding” in convolutions
  Potential additional features for neural nets, cryptography, special functions, etc., beyond those described here

## Slide 166: Hydra 4
Architecture overview
  Introduction
  Using Hydra
    Examples
    Hydra registers
    Vector instructions
    Data types
    Addressing modes
    Stored program unit
    Documentation and tools
    Hydra 4.2 functionality
    Performance
  Hardware and implementation

## Slide 167: Performance
Various projects have achieved dramatic speed-ups by applying Hydra 3 to our touch and fingerprint algorithms
  … even though Hydra’s original inspiration, “large PC touch screens,” never took off!
Some examples:
  Gian Mario Manca & Vladan Petrovic dramatically sped up OLED noise removal for touch screens in challenging noise environments
  The quantum fingerprint matcher’s image processing module runs 6x faster using Hydra 3 than as pure firmware on Prometheus’ Xtensa processor (thanks again to Vladan)
  Eric Ding’s Hydra 3 implementation of image column-wise standard deviations runs 10x faster than as pure Chimera firmware
  Karthik’s AI-based ACM algorithm runs 3.5x faster with Hydra 3 than as Chimera firmware
  Convolutional neural networks (CNNs) run over 10x faster with Hydra 3
  (And remember that Hydra 4 is 2x faster than Hydra 3 for many operations)

## Slide 168: Performance
Hydra 4 significantly outperforms SiFive’s E76 RISC-V processor …
  … even though the E76 is a full dual-issue superscalar, deeply pipelined processor
  … whose design was specifically tuned for high computational performance
Examples:
  The Byrd team reports that FFTs are ~4x faster on Hydra 4 than in E76 firmware
  Hydra 4 performs floating-point matrix multiplication 2x faster than Elkin Garcia’s firmware code, which was aggressively optimized to best fit the E76’s pipeline
    (Even though the E76, and the RISC architecture itself, has been optimized throughout its history with matrix multiplication as a key standard benchmark)
  Hydra 4.0 can accelerate byte-weighted neural network evaluation by nearly ~4x; Hydra 4.2 can accelerate the same by over 10x
  Hydra 4’s VSHA instructions are ~2x faster than the theoretically optimal assembly language E76 implementation of SHA256 (and faster still compared to practical firmware-friendly E76 code)

## Slide 169: Hydra is as fast as a supercomputer …
… if you don’t mind comparing to supercomputers that museums now use as furniture
Hydra 3 on a 116 MHz Stockholm or Rio chip can do 232 million sustained floating-point operations per second (1 add + 1 multiply on every cycle)
  Or 464 million 16-bit fixed-point ops
From a Cray-1 brochure at the Computer History Museum in Mountain View, California 
Hydra 4 at Byrd’s 400 MHz can sustain 800 million flops
  About as fast as Cray’s next machine, the quad-processor Cray X-MP
Notes: Hydra 4 on Byrd is as fast as all four cores of the quad-core Cray X-MP!

## Slide 170: Is that progress?
If the Cray-1 back in 1976 was roughly as fast as Hydra today, have we really made progress?
Hydra fits in a small portion of a small chip in a corner of your laptop or phone
Less than 0.1 mm2 in Byrd’s process
It draws a few milliwatts at most
Compared to the Cray …
Cray-1 reference manual

## Slide 171: Hardware details
The remainder of this presentation goes into the hardware and implementation details of each major block within Hydra
It will not be of interest to every reader
But if it interests you, by all means, keep reading!
…

## Slide 172: Hydra 4
Architecture overview
  Introduction
  Using Hydra
  Hardware and implementation
    Block diagram
    Host interface
    Decode and control
    Memory interfaces
    DMA channels
    Arithmetic unit (ALU)
    Stored program unit (SPU)

## Slide 173: Hydra 4
Architecture overview
  Introduction
  Using Hydra
  Hardware and implementation
    Block diagram
    Host interface
    Decode and control
    Memory interfaces
    DMA channels
    Arithmetic unit (ALU)
    Stored program unit (SPU)

## Slide 174: Block diagram
Data RAM
(shown with 4 banks)
Bus (AHB/APB/Chimera)
S
M (optional)
Bank intf
Host intf
Registers
Decode
Control
Bank intf
Bank intf
Bank intf
vmask channel
SPU channel
src1 channel
src2 channel
misc channel
dest channel
ALU
(fixed-point and floating-point datapath)
Stored program unit
hydra4.v
Mem intf
src3
dest2
Host CPU
(RISC-V, ARM, Chimera)

## Slide 175: In Byrd

## Slide 176: Port list: Clocks and control
Name | Dir | Domain | From/to | Description
hclk | In | Clock | clk_rst | Master clock
hclk_rst_n | In | hclk | clk_rst | Async reset, deassert sync’d to hclk
hydra_hclk_en | Out | hclk | clk_rst | Hydra asks to enable hclk clock gate
host_clk | In | Clock | clk_rst | Host interface clock
host_clk_rst_n | In | host_clk | clk_rst | Async reset, deassert sync’d to host_clk
hydra_host_clk_en | Out | host_clk | clk_rst | Hydra asks to enable host_clk clock gate
hclk_is_host_clk | In | hclk | clk_rst | Analogous to “!pclk_is_high_en”
hydra_awake | Out | hclk | HSO | Hydra is running and needs a clock
hydra_intr | Out | host_clk | CPU | Interrupt request to host CPU
scan_en | In | hclk | Test logic | Scan enable (for internal clock gates)
See the comments in hydra4.v for details about all these signals
All the rest of Hydra’s ports involve either host interfacing or memory interfacing

## Slide 177: Clock gating
By default, Hydra 4 includes internal clock gates (SYNA_CLK_GATE) on its hclk and host_clk clock inputs
  Chip logic can (and should) connect these to pure ungated clock sources
Hydra 4 exports hydra_hclk_en and hydra_host_clk_en signals to allow a chip to locate Hydra’s clock gating in the chip’s central clock generator instead, if desired
  Define `HYDRA_EXTERNAL_CLOCK_GATING in hydra4_config.vh to use this option
  There is a combinational logic path from the host interface (e.g., AHB HSEL and HADDR) to hydra_host_clk_en that turns on host_clk during cycles when the host accesses a Hydra register
The hydra_awake signal is used to force the chip’s master oscillator awake
  … in case the rest of the chip goes to sleep while Hydra is still operating on a vector
  This signal comes straight from a flip-flop so that it can cleanly interface to asynchronous oscillator circuits

## Slide 178: Hydra 4
Architecture overview
  Introduction
  Using Hydra
  Hardware and implementation
    Block diagram
    Host interface
    Decode and control
    Memory interfaces
    DMA channels
    Arithmetic unit (ALU)
    Stored program unit (SPU)

## Slide 179: Block diagram
Data RAM
(shown with 4 banks)
Bus (AHB/APB/Chimera)
hydra4.v
Host CPU
(RISC-V, ARM, Chimera)
M (optional)
Bank intf
Control
Bank intf
Bank intf
Bank intf
vmask channel
SPU channel
src1 channel
src2 channel
misc channel
dest channel
ALU
(fixed-point and floating-point datapath)
Stored program unit
Mem intf
src3
dest2
S
Host intf
Registers
Decode

## Slide 180: Host interface
Hydra 4 supports a choice of Chimera, AHB, APB, or “Direct” interface to the host CPU
The Chimera-style interface is much easier to integrate than Hydra 3’s
  All Chimera-facing signals are registered on host_clk == pclk_master, not on hclk
  Greatly simplifies synthesis when pclk runs at ½ hclk rate (or generally, 1/N hclk)
The AHB and APB interfaces comply with AMBA standards
  They also accommodate AHB HCLK or APB PCLK running at host_clk == hclk or 1/N hclk rate
  Byrd and SmartBridge use AHB, running at full speed (host_clk == hclk)
The Direct-style interface uses a simple handshake-free, un-pipelined protocol
Note that in non-Chimera hosts, peripheral register reads/writes tend to be slow
  For example, Byrd’s E76 CPU has a few cycles of latency for operations on its AHB system port
  The Xtensa CPU on Prometheus/Triton runs its peripheral bus at ¼ the CPU clock rate
  Unavoidable: This fact motivated Hydra 4’s opcodes-with-Vn’s design, and also its SPU

## Slide 181: Host interface: Chimera-style
Input signals no longer require multicycle_paths
  dmem_read0/write0_addr, dmem_write0_data, etc., are sampled on the host_clk rising edge (i.e., on the true pclk rising edge)
  Write data is captured in a host_clk-domain write buffer and applied during the next hclk cycle
hclk & host_clk
hclk only

## Slide 182: Host interface: Chimera-style
Output signals are now stable throughout the pclk period
  dmem_read0_data, dmem_read0/write0_ack, hydra_intr, hydra_awake, etc., change only on the host_clk rising edge, driven by host_clk-domain registers
  Hydra registers such as VL, that are only written by the host, are clocked by host_clk

## Slide 183: Host interface: Chimera-style
Some registers (such as STATUS) really must operate in the hclk domain
  These are captured in a host_clk-domain read buffer and delivered after one wait state

## Slide 184: Host interface signal timing
Hydra 4 aims for the host interface to have the simplest possible signal timing
  Every input goes only to flops clocked on host_clk
  Every output comes only from flops clocked on host_clk
  Not much logic delay in between the ports and those registers

## Slide 185: Port list: Chimera-style host interface (writing)
Name | Dir | Domain | From/to | Description
dmem_write0_request | In | host_clk | Addr dec | Standard Chimera signal
dmem_write0_ack[1:0] | Out | host_clk | Addr dec | Standard Chimera signal
dmem_write0_commit | In | host_clk | Addr dec | Standard Chimera signal
dmem_write0_addr_is_hydra | In | host_clk | Addr dec | Hydra block address decode
dmem_write0_addr_low[5:0] | In | host_clk | Addr dec | Low address bits within Hydra block
dmem_write0_size[1:0] | In | host_clk | Addr dec | Standard Chimera signal
dmem_write0_data[31:0] | In | host_clk | Addr dec | Standard Chimera signal
dmem_write0_guest_safe | Out | host_clk | Addr dec | Standard Chimera signal

## Slide 186: Port list: Chimera-style host interface (reading)
Name | Dir | Domain | From/to | Description
dmem_read0_request | In | host_clk | Addr dec | Standard Chimera signal
dmem_read0_ack[1:0] | Out | host_clk | Addr dec | Standard Chimera signal
dmem_read0_addr_is_hydra | In | host_clk | Addr dec | Hydra block address decode
dmem_read0_addr_low[5:0] | In | host_clk | Addr dec | Low address bits within Hydra block
dmem_read0_size[1:0] | In | host_clk | Addr dec | Standard Chimera signal
dmem_read0_data[31:0] | Out | host_clk | Addr dec | Standard Chimera signal
dmem_read0_guest_safe | Out | host_clk | Addr dec | Standard Chimera signal
hydra_mutex_release_out | Out | host_clk | CPU | Standard Chimera signal

## Slide 187: Host interface: AHB
The host interface complies with the AMBA 5 AHB standard (“AHB-Lite”)
  Again, all signals operate in the host_clk domain
  A write buffer and a read buffer transfer data between the hclk and host_clk domains
  Write buffer forwarding ensures the host sees the correct value if it writes a register and immediately reads it back

## Slide 188: Host interface: AHB
Hydra’s AHB host interface occasionally generates wait states to delay its response to the host’s read or write request
   When a read must go through the read buffer
   When the host reads IRQ on the very next cycle after writing to OPCODE (gives time to decode the opcode to report errors)
   For optional handshaking on writes to OPCODE and reads to G0 and G1

## Slide 189: Port list: AHB host interface
Name | Dir | Domain | From/to | Description
ahb_hsel | In | host_clk | AHB mux | Standard AHB signal
ahb_hready | In | host_clk | AHB mux | Standard AHB signal
ahb_haddr[10:0] | In | host_clk | AHB mux | Standard AHB signal (low bits only)
ahb_hprot[3:0] | In | host_clk | AHB mux | Standard AHB signal
ahb_hsize[2:0] | In | host_clk | AHB mux | Standard AHB signal
ahb_htrans[1:0] | In | host_clk | AHB mux | Standard AHB signal
ahb_hwrite | In | host_clk | AHB mux | Standard AHB signal
ahb_hwdata[31:0] | In | host_clk | AHB mux | Standard AHB signal
ahb_hrdata[31:0] | Out | host_clk | AHB mux | Standard AHB signal
ahb_hreadyout | Out | host_clk | AHB mux | Standard AHB signal
ahb_hresp | Out | host_clk | AHB mux | Standard AHB signal
The width of ahb_addr[] is given by `HYDRA_HOST_ADDR_WIDTH in hydra4_config.vh, any number from 7 to 31

## Slide 190: AHB host interface and registers
Hold
HADDR
hydra4_registers.v
HWRITE
HSIZE
hydra4_host_intf.v
HSEL
HTRANS
HREADY
Error check
HRESP
HWDATA
HRDATA
R/W buffer
rscalar special R/W
SPU special R/W
hclk- domain Registers
host_clk- domain Registers
Next value
Curr value
Curr value
Read value
Read value
R/W wait
Buffered writes
Buffered reads
IRQ, VPC, STATUS, VMCNT, PCOUNT, VnCFG
OPCODE, VL, VMA, G0, G1, IRQ, IEN, MODES, VnADDR
Instr buf ctrl
Error collect
HREADYOUT
host_clk
hclk

## Slide 191: Host interface: APB
Hydra offers an APB host interface option
  … but Hydra discourages using it, since APB is a slow protocol!

## Slide 192: Port list: APB host interface
Name | Dir | Domain | From/to | Description
apb_psel | In | host_clk | APB bridge | Standard APB signal
apb_penable | In | host_clk | APB bridge | Standard APB signal
apb_paddr[10:0] | In | host_clk | APB bridge | Standard APB signal (low bits only)
apb_pprot[2:0] | In | host_clk | APB bridge | Standard APB signal
apb_pstrb[3:0] | In | host_clk | APB bridge | Standard APB signal
apb_pwrite | In | host_clk | APB bridge | Standard APB signal
apb_pwdata[31:0] | In | host_clk | APB bridge | Standard APB signal
apb_prdata[31:0] | Out | host_clk | APB bridge | Standard APB signal
apb_pready | Out | host_clk | APB bridge | Standard APB signal
apb_pslverr | Out | host_clk | APB bridge | Standard APB signal

## Slide 193: Host interface: Direct-style
Hydra’s Direct-style host interface is a simple interface for use in chips that do not support the Chimera, AHB, or APB protocol
Very simple: No “ack” signals; no wait states; no AHB-style pipelining
Every request takes place, and completes, within one self-contained host_clk cycle

## Slide 194: Port list: Direct host interface
Name | Dir | Domain | From/to | Description
hydra_host_req | In | host_clk | Periph bus | Request a read or write
hydra_host_write | In | host_clk | Periph bus | This request is for a write vs read
hydra_host_addr[6:0] | In | host_clk | Periph bus | Byte address of register (low bits only)
hydra_host_size[1:0] | In | host_clk | Periph bus | Access size (0=byte, 1=short, 2=long)
hydra_host_priv | In | host_clk | Periph bus | High if access is from privileged code
hydra_host_wdata[31:0] | In | host_clk | Periph bus | Data to write on this cycle
hydra_host_rdata[31:0] | Out | host_clk | Periph bus | Data that was read on this cycle
hydra_host_error | Out | host_clk | Periph bus | High if this access request is invalid

## Slide 195: Hydra 4
Architecture overview
  Introduction
  Using Hydra
  Hardware and implementation
    Block diagram
    Host interface
    Decode and control
    Memory interfaces
    DMA channels
    Arithmetic unit (ALU)
    Stored program unit (SPU)

## Slide 196: Block diagram
Data RAM
(shown with 4 banks)
Bus (AHB/APB/Chimera)
hydra4.v
Host CPU
(RISC-V, ARM, Chimera)
M (optional)
Bank intf
Control
Bank intf
Bank intf
Bank intf
vmask channel
SPU channel
src1 channel
src2 channel
misc channel
dest channel
ALU
(fixed-point and floating-point datapath)
Stored program unit
Mem intf
src3
dest2
S
Host intf
Registers
Decode

## Slide 197: Instruction decoding
The Decode block receives the 30-bit opcode when the host writes to OPCODE
  Also the current values of “instruction buffered” registers: VL, VMA, G0, G1, MODES.ROUND
  And the four VnCFG’s and VnADDR’s selected by the low bits of the opcode:
The decoder validates the instruction
  Adjusts IRQ.ERROR quickly enough so the host can see the error code, even if it reads IRQ immediately after writing to OPCODE
The decoder pre-processes the instruction to simplify downstream processing
  For example, instructions that write to the vector mask are converted to a K=1 packed vector dest
  Instructions written to COMPAT_OPCODE are fully translated from Hydra 3 to Hydra 4
The decoder captures the instruction into a holding buffer
  This represents the first stage of the instruction buffer as seen by the user

## Slide 198: Instruction control
The Control block receives the instruction from the decoder when it is ready
  If Hydra was idle when the user wrote to OPCODE: On the very next hclk
  If Hydra was already running an instruction: When the current instruction finishes
The controller captures the instruction for execution
  This is the second stage of the instruction buffer
  The instruction buffer is expensive! 228 + 6*W flops for each stage
  But double-buffering the instructions greatly improves performance
  The host can set up the next vector operation while the current operation is still running
  In most cases, double-buffering completely eliminates this instruction setup overhead

## Slide 199: Instruction control
The controller sends the instruction to the various channels and the ALU
  Currently, there is not much additional processing or “state” in the controller itself
Eventually, the controller will implement “instruction joining”
  Hydra can begin reading the next instruction’s src operands while the current instruction is still finishing up in the ALU and dest channel
  This feature is defined in the Hydra 4 User’s Guide, but not yet implemented in Hydra 4.0–4.2
    There was not enough time for it in the Byrd and SmartBridge project schedules

## Slide 200: Instruction joining
Hydra 3’s and 4.2’s pipeline can do only one instruction at a time
  Instruction A must complete all its dest writes before B can read any src
  Works correctly even if any destA[i] is the same address as any srcB[j]
Hydra 4.x will be able to optimize this in cases when destA and srcB do not overlap, or when they have only a “simple” overlap

## Slide 201: Hydra 4
Architecture overview
  Introduction
  Using Hydra
  Hardware and implementation
    Block diagram
    Host interface
    Decode and control
    Memory interfaces
    DMA channels
    Arithmetic unit (ALU)
    Stored program unit (SPU)

## Slide 202: Block diagram
Data RAM
(shown with 4 banks)
Bus (AHB/APB/Chimera)
hydra4.v
Host CPU
(RISC-V, ARM, Chimera)
M (optional)
Bank intf
Control
Bank intf
Bank intf
Bank intf
vmask channel
SPU channel
src1 channel
src2 channel
misc channel
dest channel
ALU
(fixed-point and floating-point datapath)
Stored program unit
Mem intf
src3
dest2
S
Host intf
Registers
Decode

## Slide 203: Memory interfaces
By default, Hydra 4 exports one memory interface for each RAM bank
  Each bank interface connects directly to one banked RAM
  hydra4_config.vh configures the number of banks (Byrd and SmartBridge have 4 banks)
  It also configures the address pattern for each bank
Preferably, a chip arranges its data RAM in interleaved banks
  I.e., the bank address patterns are configured to use the low address bits (bits 3:2 or bits 4:2) to select the bank
Arbitration among banks takes place inside the Hydra core
  Each bank interface sees only addresses in that bank
  The arbitration is isolated by a pipeline stage from port-level bus signal timing
Every bank may do an 8-, 16-, or 32-bit-wide read or write on every cycle

## Slide 204: Memory interfaces
If an address does not fall in any bank…
  By default, this is flagged as a bus error
  Hydra 4 has an optional “General Memory port”
  If it is present, non-bank accesses go out on this port
  Typically the General Memory port would go to the chip’s bus matrix, e.g., to allow Hydra to “DMA” into peripherals, Flash, or other memories
  (Byrd A0 and SB7900 do not have a general memory port: No need to DMA into DAQ/DASE or other peripherals; uncached Flash is too slow for direct access to be useful)
  (But Byrd B0 uses it to connect Hydra to SYS_MEM RAM)
If W is configured with just enough address bits to cover the entire data RAM (e.g., as it is on Byrd and SmartBridge) …
  Then every possible address falls in one of the banks
  … and a General Memory port is not needed or useful

## Slide 205: Memory protocol options
Hydra 4 offers two types of signaling for its RAM interfaces:
  Direct style (similar to Hydra 3’s RAM signaling)
  AHB style
The main difference is whether write data and “ack” are pipelined
  This also affects the behavior of request/addr/size signals during wait states
The “Direct” method is more efficient and easier to work with
  Very similar to the “tightly coupled RAM” interface of many commercial MCUs
  Byrd and SmartBridge use it for their direct Hydra-to-RAM interfaces instead of AHB-style
  Note that this signaling convention is not the same as Chimera’s dmem_read/write bus signaling
  But it is much like how Hydra 3 accessed the RAM in prior Chimera-based chips
The Banked Memory and General Memory interfaces can each independently choose either Direct or AHB signaling

## Slide 206: Memory interface signals
Direct style 
AHB style 
(HSEL/HTRANS)
(HWRITE)
(HADDR)
(HREADYOUT)
(HREADY)
(HRDATA)
(HWDATA)
(HRESP)
Wait state on read
Wait state on write

## Slide 207: Memory interface signal timing
The memory interface operates in the hclk clock domain
Most memory interface signals have little logic delay between ports and flops
One exception: hydra_ramN_ack
  Hydra has significant logic between this port and its internal flops
  Is this acceptable? (Initial synthesis results say “yes”)
  These are among the worst Hydra timing paths in the synthesis report (but better than the worst E76 paths)
  Hydra’s RTL has an option to pipeline this signal, but it is expensive (many gates and flops) so we didn’t use it for Byrd A; we did need it for Byrd B
Previously, the worst timing path was from hydra_ramN_rdata to the many channel FIFOs
  This has already been fixed with a pipeline stage (also expensive — optional, but needed in Byrd!)

## Slide 208: Port list: RAM bank interface (if Direct-style)
Name | Dir | Domain | From/to | Description
hydra_ramN_req | Out | hclk | RAM bank N | Request a read or write
hydra_ramN_ack[1:0] | In | hclk | RAM bank N | RAM can perform the current request
hydra_ramN_addr[W-1:0] | Out | hclk | RAM bank N | W = `HYDRA_WIDTH_W in config.vh
hydra_ramN_write | Out | hclk | RAM bank N | Current request is a write
hydra_ramN_size[1:0] | Out | hclk | RAM bank N | Current request data size (8, 16, or 32)
hydra_ramN_rdata[31:0] | In | hclk | RAM bank N | RAM read data (delayed 1 hclk)
hydra_ramN_wdata[31:0] | Out | hclk | RAM bank N | Current RAM write data
hydra_ramN_ready | Out | hclk | — | (Unused for Direct-style)
hydra_ramN_error | In | hclk | — | (Supported but typically unused and tied low for direct-style memories)
Repeated for each N = 0 … `HYDRA_NUM_BANKS−1
These signals operate much like the old Hydra 3 RAM interface signals
  (Except that bank arbitration happens inside Hydra instead of in the RAM controller)

## Slide 209: Port list: RAM bank interface (if AHB-style)
Name | Dir | Domain | From/to | Description
hydra_ramN_req | Out | hclk | RAM bank N | Connect to AHB HSEL
hydra_ramN_ack | In | hclk | RAM bank N | Connect to AHB HREADYOUT
hydra_ramN_addr[W-1:0] | Out | hclk | RAM bank N | Connect to AHB HADDR[W-1:0]
hydra_ramN_write | Out | hclk | RAM bank N | Connect to AHB HWRITE
hydra_ramN_size[2:0] | Out | hclk | RAM bank N | Connect to AHB HSIZE (8, 16, or 32 bits)
hydra_ramN_rdata[31:0] | In | hclk | RAM bank N | Connect to AHB HRDATA
hydra_ramN_wdata[31:0] | Out | hclk | RAM bank N | Connect to AHB HWDATA
hydra_ramN_ready | Out | hclk | RAM bank N | Connect to AHB HREADY
hydra_ramN_error | In | hclk | RAM bank N | Connect to AHB HRESP
Repeated for each N = 0 … `HYDRA_NUM_BANKS−1
Note: hydra_ramN_wdata, _ready, _error are delayed 1 hclk relative to Direct-style
Also connect HBURST = 3’b000, HPROT = 4’b0001, HMASTLOCK = 1’b0 and HTRANS = { hydra_ramN_req, 1’b0 }

## Slide 210: Port list: General Direct-style master interface
Name | Dir | Domain | From/to | Description
gen_mem_req | Out | hclk | Gen RAM | Request a read or write
gen_mem_ack[1:0] | In | Hclk | Gen RAM | RAM can perform the current request
gen_mem_addr[W-1:0] | Out | hclk | Gen RAM | W = `HYDRA_WIDTH_W in config.vh
gen_mem_prot | Out | hclk | Gen RAM | Current request is a privileged access
gen_mem_write | Out | hclk | Gen RAM | Current request is a write
gen_mem_size[1:0] | Out | hclk | Gen RAM | Current request data size (8, 16, or 32)
gen_mem_rdata[31:0] | In | hclk | Gen RAM | RAM read data (delayed 1 hclk)
gen_mem_wdata[31:0] | Out | hclk | Gen RAM | Current RAM write data
gen_mem_error | In | hclk | Gen RAM | (Supported but typically unused and tied low for direct-style memories)

## Slide 211: Port list: General AHB master interface
Name | Dir | Domain | From/to | Description
gen_mem_hsel | Out | hclk | AHB mux | Standard AHB signal
gen_mem_hready | Out | Hclk | AHB mux | Standard AHB signal
gen_mem_haddr[W-1:0] | Out | hclk | AHB mux | Standard AHB signal
gen_mem_hprot[3:0] | Out | hclk | AHB mux | Standard AHB signal
gen_mem_hsize[2:0] | Out | hclk | AHB mux | Standard AHB signal (8, 16, or 32 bits)
gen_mem_htrans[1:0] | Out | hclk | AHB mux | Standard AHB signal (IDLE or NONSEQ)
gen_mem_hburst[2:0] | Out | hclk | AHB mux | Standard AHB signal (always 3’b000)
gen_mem_hwrite | Out | hclk | AHB mux | Standard AHB signal
gen_mem_hmastlock | Out | hclk | AHB mux | Standard AHB signal (always 1’b0)
gen_mem_hwdata[31:0] | Out | hclk | AHB mux | Standard AHB signal
gen_mem_hrdata[31:0] | In | hclk | AHB mux | Standard AHB signal
gen_mem_hreadyout | In | hclk | AHB mux | Standard AHB signal
gen_mem_hresp | In | hclk | AHB mux | Standard AHB signal

## Slide 212: Memory interfaces
hydra4_bank_intf.v
Priority
Round-robin
(×6 channels)
masked
taken_out
taken_in
req
Bank match
Cur_chan
Cur_chan _r1
Cur_chan _r2
addr
wdata
size, write
addr
req
rdata, rdata_push
ack, wdata_pop
(Direct)
(AHB)
wdata
ack
rdata
size, write
Hold
Taken
wait
commit
pending_writes
pending_reads
(optional extra pipe stage)
(optional add’l pipe stage)
← To memory
To DMA channels →
size, write, masked, addr
select chan
(×N banks)

## Slide 213: Hydra 4
Architecture overview
  Introduction
  Using Hydra
  Hardware and implementation
    Block diagram
    Host interface
    Decode and control
    Memory interfaces
    DMA channels
    Arithmetic unit (ALU)
    Stored program unit (SPU)

## Slide 214: Block diagram
Data RAM
(shown with 4 banks)
Bus (AHB/APB/Chimera)
hydra4.v
Host CPU
(RISC-V, ARM, Chimera)
M (optional)
Bank intf
Control
Bank intf
Bank intf
Bank intf
vmask channel
SPU channel
src1 channel
src2 channel
misc channel
dest channel
ALU
(fixed-point and floating-point datapath)
Stored program unit
Mem intf
src3
dest2
S
Host intf
Registers
Decode

## Slide 215: DMA channels
Hydra 4 internally has six channels for transferring data to or from memory
  A read-only src1 channel
  A read-only src2 channel
  A write-only dest channel
  A “misc” channel which can either read src3 or write dest2 (depending on the instruction)
  A special read-only channel for reading vector masks
  A special channel for reading SPU programs and performing SPU loads/stores
These channels contend with each other for access to the RAM bank interfaces
  Each channel wants to talk to one bank according to its current RAM address
  When several channels all want to use the same bank, Hydra uses a priority rule first, then round-robin arbitration if RAM contention persists

## Slide 216: DMA channels
As shown earlier, Hydra (like the Cray-1 and other vector machines) needs to perform multiple parallel reads and writes per cycle to keep its data pipeline busy
  Interleaved banks of RAM allow Hydra to do this automatically, with no user intervention
  Hydra does not require users to manage the location or alignment of vectors in RAM
  Hydra’s channel FIFOs make this possible
Fetch B | B[0] | B[1] | B[2] | B[3] | B[4] | B[5] | B[6] | B[7] | B[8] | B[9] |  |  |  | 
Fetch C |  | C[0] | C[1] | C[2] | C[3] | C[4] | C[5] | C[6] | C[7] | C[8] | C[9] |  |  | 
Exec (1) |  |  | [0] | [1] | [2] | [3] | [4] | [5] | [6] | [7] | [8] | [9] |  | 
Exec (2) |  |  |  | [0] | [1] | [2] | [3] | [4] | [5] | [6] | [7] | [8] | [9] | 
Write A |  |  |  |  | A[0] | A[1] | A[2] | A[3] | A[4] | A[5] | A[6] | A[7] | A[8] | A[9]
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0000 |  |  |  |  |  |  |  | 
0001 |  |  |  |  |  |  |  | 
0002 |  |  |  |  |  |  |  | 
0003 |  |  |  |  |  |  |  | 
0004 |  |  |  |  |  |  |  | 
0005 |  |  |  |  |  |  |  | 
0006 |  |  |  |  |  |  |  | 
0007 |  |  |  |  |  |  |  | 
0008 |  |  |  |  |  |  |  | 
0009 |  |  |  |  |  |  |  | 
000A |  |  |  |  |  |  |  | 
000B |  |  |  |  |  |  |  | 
000C |  |  |  |  |  |  |  | 
000D |  |  |  |  |  |  |  | 
000E |  |  |  |  |  |  |  | 
000F |  |  |  |  |  |  |  | 
0010 |  |  |  |  |  |  |  | 
0011 |  |  |  |  |  |  |  | 
0012 |  |  |  |  |  |  |  | 
0013 |  |  |  |  |  |  |  | 
0014 |  |  |  |  |  |  |  | 
0015 |  |  |  |  |  |  |  | 
0016 |  |  |  |  |  |  |  | 
0017 |  |  |  |  |  |  |  | 
0018 |  |  |  |  |  |  |  | 
0019 |  |  |  |  |  |  |  | 
001A |  |  |  |  |  |  |  | 
001B |  |  |  |  |  |  |  | 
001C |  |  |  |  |  |  |  | 
001D |  |  |  |  |  |  |  | 
001E |  |  |  |  |  |  |  | 
001F |  |  |  |  |  |  |  | 
0020 |  |  |  |  |  |  |  | 

## Slide 217: RAM read/write channels with FIFOs
Hydra’s several channels to RAM operate simultaneously and independently
Each RAM channel has a FIFO (first-in/first-out) data buffer
src1 data
src2 data
dest data
Read FIFO
Read FIFO
Write FIFO
Banked RAM
Arithmetic Unit

## Slide 218: RAM read/write channels with FIFOs
The read and write FIFOs create some “slack” in the pipeline
This makes Hydra extremely tolerant of arbitrary vector alignments
Hydra starts by reading both source vectors simultaneously
  If the arrays’ alignment in RAM is such that B[i] falls in a different bank than C[i] for every i …
  … and likewise there is no conflict when writing to A[i] …
  … then everything is simple:
Fetch B | B[0] | B[1] | B[2] | B[3] | B[4] | B[5] | B[6] | B[7] | B[8] | B[9] |  |  |  | 
Fetch C | C[0] | C[1] | C[2] | C[3] | C[4] | C[5] | C[6] | C[7] | C[8] | C[9] |  |  |  | 
Exec (1) |  | [0] | [1] | [2] | [3] | [4] | [5] | [6] | [7] | [8] | [9] |  |  | 
Exec (2) |  |  | [0] | [1] | [2] | [3] | [4] | [5] | [6] | [7] | [8] | [9] |  | 
Write A |  |  |  | A[0] | A[1] | A[2] | A[3] | A[4] | A[5] | A[6] | A[7] | A[8] | A[9] | 
Banked RAM
Arith Unit
“B”
“C”
“A”

## Slide 219: RAM read/write channels with FIFOs
Suppose B[i] lands in the same bank as C[i], because B and C are similarly aligned in RAM
  Hydra will fetch B[0] on the first cycle …
  … but its attempt to fetch C[0] at the same time will stall due to a bank conflict
  Hydra will hold B[0] in its channel FIFO while it tries to read C[0] again on the next cycle
  The “B” RAM channel simultaneously reads B[1], which also succeeds because B[1] and C[0] fall in different banks
    They must, since B[1] and B[0] are in different interleaved banks while B[0] and C[0] were in the same bank
Fetch B | B[0] | B[1] |  |  |  |  |  |  |  |  |  |  |  | 
Fetch C | stall | C[0] |  |  |  |  |  |  |  |  |  |  |  | 
Exec (1) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Exec (2) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Write A |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Banked RAM
Arith Unit
“B”
“C”
“A”

## Slide 220: RAM read/write channels with FIFOs
Hydra quickly falls into a pattern fetching B[i+1] together with C[i] on each cycle “i”, free of bank conflicts
  The “B” FIFO always holds one data value: It pushes and pops one value on every cycle
  The “C” FIFO always passes its data straight through
No special attention is required by the user
Firmware can casually allocate arrays like B and C without micro-managing their location and alignment
Fetch B | B[0] | B[1] | B[2] | B[3] | B[4] | B[5] | B[6] | B[7] | B[8] | B[9] |  |  |  | 
Fetch C | stall | C[0] | C[1] | C[2] | C[3] | C[4] | C[5] | C[6] | C[7] | C[8] | C[9] |  |  | 
Exec (1) |  |  | [0] | [1] | [2] | [3] | [4] | [5] | [6] | [7] | [8] | [9] |  | 
Exec (2) |  |  |  | [0] | [1] | [2] | [3] | [4] | [5] | [6] | [7] | [8] | [9] | 
Write A |  |  |  |  | A[0] | A[1] | A[2] | A[3] | A[4] | A[5] | A[6] | A[7] | A[8] | A[9]
Banked RAM
Arith Unit
“B”
“C”
“A”

## Slide 221: RAM read/write channels with FIFOs
Now suppose A[0] also lands so that it would conflict with the reads of B[4] and C[4]
Hydra absorbs two results into its write-channel FIFO as it waits for a chance to write to A
Again, it naturally falls into a pattern where RAM accesses go at full speed with no conflicts
For these particular vector alignments, the steady state is:
  FIFO “B” always holds one value, pushing and popping each time;
  FIFO “C” always passes straight through;
  FIFO “A” always holds two values, pushing and popping each time
Fetch B | B[0] | B[1] | B[2] | B[3] | B[4] | B[5] | B[6] | B[7] | B[8] | B[9] |  |  |  | 
Fetch C | stall | C[0] | C[1] | C[2] | C[3] | C[4] | C[5] | C[6] | C[7] | C[8] | C[9] |  |  | 
Exec (1) |  |  | [0] | [1] | [2] | [3] | [4] | [5] | [6] | [7] | [8] | [9] |  | 
Exec (2) |  |  |  | [0] | [1] | [2] | [3] | [4] | [5] | [6] | [7] | [8] | [9] | 
Write A |  |  |  |  | stall | stall | A[0] | A[1] | A[2] | A[3] | A[4] | A[5] | A[6] | A[7]
Banked RAM
Arith Unit
“B”
“C”
“A”

## Slide 222: RAM read/write channels with FIFOs
Hydra shares access to the RAM with the host CPU and (in some chips) with other DMA peripherals
  The host CPU and DMA get top priority, and Hydra’s FIFOs soak up the resulting stalls naturally
 Each RAM-read channel issues “read” requests to RAM as fast as it can go
 The RAM-write channel deposits results to RAM as fast as the RAM can take them
 If a FIFO ever fills to capacity (~4 items), the pipeline stalls upstream to relieve “back pressure”
 If a FIFO ever runs empty, the pipeline stalls downstream until more data is available
Fetch B | B[0] | B[1] | B[2] | B[3] | B[4] | B[5] | B[6] | B[7] | stall | B[8] | B[9] |  |  |  |  | 
Fetch C | stall | C[0] | C[1] | C[2] | C[3] | C[4] | stall | C[5] | C[6] | C[7] | C[8] | C[9] |  |  |  | 
Exec (1) |  |  | [0] | [1] | [2] | [3] | [4] | — | [5] | [6] | [7] | [8] | [9] |  |  | 
Exec (2) |  |  |  | [0] | [1] | [2] | [3] | [4] | — | [5] | [6] | [7] | [8] | [9] |  | 
Write A |  |  |  |  | A[0] | A[1] | A[2] | A[3] | A[4] | — | A[5] | A[6] | A[7] | stall | A[8] | A[9]

## Slide 223: Bank contention for linear vectors
This timing diagram (from actual simulation results, as shown in the Hydra User’s Guide) shows a VMADD instruction with four linear (stride-1) vectors
  The vector base addresses have been chosen to create worst-case bank contention
  All three source vectors start in bank 2, causing two bank-conflict stalls at the start (in yellow)
  The dest vector starts in bank 0, which happens to be busy serving src1, then src2, then src3 at time 12 when the first result emerges from the pipeline: This causes three more stalls
  Once the FIFOs have absorbed the stalls, operation continues at full speed

## Slide 224: Bank contention for strided vectors
When a vector’s stride is a multiple of 4 (actually, a multiple of the number of RAM banks), every element in it will fall in the same bank
  This can slow Hydra noticeably even if the other vectors are linear 
  And it can slow down dramatically if the vectors are aligned the same and all are stride-4! 

## Slide 225: Channels: Other functions
The channel’s sequencer counts cycles to determine when the channel is done
  … and it counts the nested sub-cycles of matrices and convolutions
The address generator produces a sequence of RAM addresses for the selected addressing mode
  For linear mode and stride mode: Simple addition
  For matrix addressing: Add either the row stride or the column stride
  Special formulas for FFT addressing, matrix multiply, convolutions, etc.
Sketch of address generation for src1  in 2D convolutions

## Slide 226: Channels: Other functions
Also…
A source unpacker or dest packer for packed addressing mode
  It also realigns 16- or 8-bit data into the appropriate lanes of memory wdata/rdata
  And merges adjacent byte/short reads or writes into 32-bit accesses when possible
  And it is used for instructions that generate a vector mask
Logic to handle incoming vector masks
  With a parallel FIFO for “mask” bits and a few other control bits
  The channel suppresses the RAM read or RAM write for any masked-out vector element
Extra pipeline stages in several places to help meet 400 MHz timing

## Slide 227: DMA channel (each of src1, src2, dest, misc)
hydra4_channel.v
count
column_count
kernel_count
kernel_column_count
addr
row_addr
outer_addr
outer_row_addr
src1 only
src1 only
Sequencer
Address generator
start
Column stride
FFT adjust
Packing stride
Index value
<<
+
esize
active
advance
done
first
last
final
select_row
Row stride
Front
Unpack
Pack
writing, rscalar, pattern
addr
rdata
alu_dest
first, last, masked
alignment info
Mask logic
Channel FIFO
special R/W
Control
FIFO
Tag FIFO
Align FIFO

## Slide 228: Vector mask channel
There is a specialized, read-only channel for vector masks
It reads 32-bit words from the vector mask and holds the most recent two words
  This is enough to cover the current mask bit of every active src and dest channel
  It sends the relevant mask bits to all the channels depending on each channel’s current count
Eventually, Hydra 4.x will support “vector mask optimization”
  Each channel can see the next several upcoming mask bits
  The channel can skip multiple iterations when conditions are right
  If the next 2K mask bits are visible and they are all ‘0’s, then linear or strided addressing can skip through 2K iterations at once: Adjust the address by (stride << K) instead of by (stride)
  If all the channels are able to skip in this way, Hydra can run quickly on “sparse” masked vectors
  Hydra 3’s design made this impossible, but Hydra 4 is architected to allow it
  This feature is defined in the Hydra 4 User’s Guide, but not yet implemented in Hydra 4.0–4.2

## Slide 229: Hydra 4
Architecture overview
  Introduction
  Using Hydra
  Hardware and implementation
    Block diagram
    Host interface
    Decode and control
    Memory interfaces
    DMA channels
    Arithmetic unit (ALU)
    Stored program unit (SPU)

## Slide 230: Block diagram
Data RAM
(shown with 4 banks)
Bus (AHB/APB/Chimera)
hydra4.v
Host CPU
(RISC-V, ARM, Chimera)
M (optional)
Bank intf
Control
Bank intf
Bank intf
Bank intf
vmask channel
SPU channel
src1 channel
src2 channel
misc channel
dest channel
ALU
(fixed-point and floating-point datapath)
Stored program unit
Mem intf
src3
dest2
S
Host intf
Registers
Decode

## Slide 231: Arithmetic unit
Hydra 4 has a single arithmetic pipeline for all data types (integer, fixed, float, Posit)
Hydra 4’s pipeline has many more stages than Hydra 3’s
  But actually, Hydra 3’s float pipeline ran at half speed …
  … so it took four hclk’s for a multiply-add
  … and Hydra 4 is designed to clock significantly faster than before
  SiFive’s E76 CPU has 5-cycle latency, too, for floating-point operations
It’s a fact: A chip this fast needs a deep pipeline!
  The long pipeline does not hurt throughput, but it affects instruction startup time
src1
src2
src3
dest
Unpack, negate
Prep
Shift
Normalize
Shift, round, saturate
Channel packer
Multiply 1
Multiply 2
Wide adder
= src1 + (src2*src3)

## Slide 232: Arithmetic pipeline
The ALU pipeline advances once per hclk cycle
It consumes one value from each source channel (src1, src2, src3) whenever all three channels have a value available in their channel FIFOs
  Otherwise (e.g., if RAM bank contention slows one src), a “bubble” passes through the pipeline for that cycle
src1
src2
src3
dest
Unpack, negate
Prep
Shift
Normalize
Shift, round, saturate
Channel packer
Multiply 1
Multiply 2
Wide adder
(Stage 2)
(Stage 3)
(Stage 4)
(Stage 5)
(Stage 6)
(Stage 1)
VMUL on 8-element vectors with 3 stall cycles

## Slide 233: Arithmetic pipeline
When live data is in the output stage, it goes to the dest channel
  Or the ALU pipeline stalls if the dest channel is not ready to accept data (dest FIFO is full)
For simple vector operations, data flows through at a rate of one multiply-add calculation per hclk
  (But with several hclk’s of latency)
Some instructions (such as VCRC) have different execution patterns, controlled by a simple state machine in the ALU
  For simplicity, Hydra 4.0–4.2 uses the same six-stage pipeline structure for all instructions
src1
src2
src3
dest
Unpack, negate
Prep
Shift
Normalize
Shift, round, saturate
Channel packer
Multiply 1
Multiply 2
Wide adder
(Stage 2)
(Stage 3)
(Stage 4)
(Stage 5)
(Stage 6)
(Stage 1)

## Slide 234: Numbers
Hydra 4’s ALU operates internally on a special internal float-like format
  A 9-bit integer exponent E and a 33-bit integer significand F
  The numeric value is 2E * F
  Both components are signed integers in two’s complement notation
  Plus a few extra bits to encode the special values 0, , and NaN
  This format can express all numbers that are representable in all of Hydra’s data types
The ALU datapath converts all inputs to this form in its input stage
  Thus, Hydra instructions can have any mixture of data types: E.g., float32 ← int32 * float16
The datapath converts results back to the desired data type in its output stage

## Slide 235: Internal number format
Format | Exponent (9 bits 2s-comp) | Significand (33 bits 2s-comp) | Notes
float32 | Add bias | Signed fraction | To convert to internal format, negate if sign=1 and insert an explicit leading ‘1’ if not denormal To convert from this format, negate if negative, round, and normalize
bfloat16 | Add bias | Signed fraction | 
float16 | Add bias | Signed fraction | 
int | 0 | Sign-extend | Significand can be treated as a 33-bit signed integer
unsigned | 0 | Zero-extend | 
fixed SQ.k | −k | Sign-extend | 
fixed UQ.k | −k | Zero-extend | 
posit | Variable size | Sign-extend | Special conversion rules

## Slide 236: Multiply-accumulate
The VMAC instruction computes a sum of products
Challenge: How to accumulate efficiently when the latency through the pipeline is many cycles?
When (src1, src2, src3) are all integers or fixed-point numbers:
  The addition step is a simple integer add, which can be done with one-cycle latency
  A 96-bit accumulator calculates the mathematically exact sum (up to 231 products of pairs of 33-bit signed numbers), giving a precise and deterministic result
src1
src2
src3
dest
Unpack, negate
Prep
Shift
Normalize
Shift, round, saturate
Channel packer
Multiply 1
Multiply 2
Wide adder
(Stage 2)
(Stage 3)
(Stage 4)
(Stage 5)
(Stage 6)
(Stage 1)

## Slide 237: Multiply-accumulate
When floating-point inputs are involved:
  The natural loop latency around the “addend” side of the ALU is four cycles
  Hydra 4 offers several flavors of MAC instruction to deal with this
VOMAC (“ordered accumulate”):
  Emulates a simple “for” loop iterating over the vector elements from left to right
  It really does take 4 cycles per iteration!
  VOMAC runs 4x slower than normal vector instructions
  Hydra provides the VOMAC instruction for completeness, but it is not satisfying and will rarely be used in practice
src1
src2
src3
dest
Unpack, negate
Prep
Shift
Normalize
Shift, round, saturate
Channel packer
Multiply 1
Multiply 2
Wide adder
(Stage 2)
(Stage 3)
(Stage 4)
(Stage 5)
(Stage 6)
(Stage 1)

## Slide 238: Multiply-accumulate
VDMAC (“deterministic accumulate”):
  Runs at full speed
  Still recirculates the ALU with 4-cycle latency
  Result: Four partial sums will circulate around inside the ALU, each one summing 1/4 of all the elements
  At the end, VDMAC runs a few irregular cycles to collect and sum together the four partial sums
  Orchestrated by a simple state machine in the ALU’s control logic
src1
src2
src3
dest
Unpack, negate
Prep
Shift
Normalize
Shift, round, saturate
Channel packer
Multiply 1
Multiply 2
Wide adder
(Stage 2)
(Stage 3)
(Stage 4)
(Stage 5)
(Stage 6)
(Stage 1)

## Slide 239: Multiply-accumulate: VDMAC sequencing
AB = A + B; CD = C + D; Σ = A + B + C + D
Notes: Why does this diagram show 5 ALU stages when the previous slide showed 7? First, because this operation has a 32-bit result type so the “channel packer” stage can be bypassed. That leaves an ALU with 6 stages of processing sandwiched between 7 registers. The first and last of those registers correspond to the FIFO buffers shown in the diagram here, leaving 5 internal register stages in the ALU.

## Slide 240: Multiply-accumulate: VDMAC sequencing
https://safelyendangered.com
AB = A + B; CD = C + D; Σ = A + B + C + D

## Slide 241: Multiply-accumulate: Rounding error
VDMAC will not give quite the same result as VOMAC
Their floating-point rounding errors will not match:
  Floating-point addition does not obey the associative law of “true” addition
  For example, “1.0 + (10−10) − 1.0” gives 0.0 instead of 10−10 when evaluated naturally (from left to right) using single-precision floats
  10−10 is so small, it rounds away to nothing when added to 1.0 in single-precision
  Therefore, the calculation gets a very different answer than “1.0 − 1.0 + (10−10)”, even though they are mathematically equivalent!
However, VDMAC’s result can be precisely reproduced by a reasonably simple and deterministic firmware loop
  Hence the “D” in “VDMAC”

## Slide 242: Multiply-accumulate
VMAC (“fast accumulate”):
  Most ordinary multiply-accumulations should use the plain “VMAC” instruction
  Runs at full speed
  For fixed-point operands, it runs as shown earlier
  For floating-point operands, VMAC runs like VDMAC but (potentially) with higher precision accumulations that give better results …
  … but would be hard to reproduce exactly in host CPU firmware
  (Note that higher-precision float VMAC is not yet implemented; in Hydra 4.0–4.2, VMAC on floats currently works exactly the same as VDMAC)
src1
src2
src3
dest
Unpack, negate
Prep
Shift
Normalize
Shift, round, saturate
Channel packer
Multiply 1
Multiply 2
Wide adder
(Stage 2)
(Stage 3)
(Stage 4)
(Stage 5)
(Stage 6)
(Stage 1)

## Slide 243: ALU: Other operations
The Hydra 4 User’s Guide defines a wide variety of operations on vectors:
  Bitwise operations
  Various flavors of MIN / MAX
  Hamming distance
  Cryptographic functions, etc.
  Find, compress, expand, gather, scatter, …
  Fast medians
  Integer and float division in all rounding modes
  Fast SIMD treatment of 16-bit integer arithmetic
  Optimized treatment of sparse vector masks
  Padding for convolutions
  Instruction joining
The ones in red were not implemented in Hydra 4.0–4.2 on SmartBridge and Byrd
  Future chips can include these and other improvements in Hydra 4.3 or later

## Slide 244: Hydra 4
Architecture overview
  Introduction
  Using Hydra
  Hardware and implementation
    Block diagram
    Host interface
    Decode and control
    Memory interfaces
    DMA channels
    Arithmetic unit (ALU)
    Stored program unit (SPU)

## Slide 245: Block diagram
Data RAM
(shown with 4 banks)
Bus (AHB/APB/Chimera)
hydra4.v
Host CPU
(RISC-V, ARM, Chimera)
M (optional)
Bank intf
Control
Bank intf
Bank intf
Bank intf
vmask channel
SPU channel
src1 channel
src2 channel
misc channel
dest channel
ALU
(fixed-point and floating-point datapath)
Stored program unit
Mem intf
src3
dest2
S
Host intf
Registers
Decode

## Slide 246: Stored program unit
The stored program unit is designed to be simple
It has a simple channel to read SPU instructions
  Normally it reads consecutive words into a FIFO buffer
  The decoder pops words from the FIFO and executes them
  A branch instruction flushes the FIFO and restarts the channel reading from a new address
  Load/store instructions stop the FIFO, run a single read or write, then restart the channel as if upon a branch
The SPU can read or write one Hydra register on each cycle using a “special R/W” interface to the registers block
SPU instructions that do more than one read or write are sequenced into several cycles
  The SPU is not meant to be a high-performance CPU!

## Slide 247: Stored program unit
hydra4_spu.v
Instr FIFO
Decode
Holding
State machine
rdata
Addr
vpc
Special R/W
CMP condition
post an opcode
SPU DMA channel
<<
+/−
+4
(to registers)

## Slide 248
Thank You